Day 5: Wide-Field Issues

---
Before we start...
$ cd ~/Workshop2008
$ svn up

---
The Full-Sky ME
size 24 { "ME of a single point:" } newline {bold V}_pq = {bold J}_p {bold B} {bold J}^{ %dagger }_q newline size 24 {"The sky has a brightness density: "} {bold B}(vec %sigma) newline size 24 {"(where " vec %sigma " is a unit direction vector)"} newline size 24 {"So the total visibility is obtained by integrating over a sphere:"} newline newline {bold V}_pq = int csub {"sky"} {bold J}_p(vec %sigma){bold B}(vec %sigma){bold J}^{%dagger}_q(vec %sigma)d%OMEGA newline newline size 24 { "This is not very useful, so we project " bold B " onto " } newline size 24 { "the " %l%m " plane, tangential at the phase centre..." } newline

---
The Full-Sky ME
size 22{ "When projecting an integral, we must also project the integration volume:"} newline size 24 { d%OMEGA = {d%l d%m} over sqrt{1-%l^2-%m^2} = {d%l d%m} over %n, } newline size 22 { "and in the " %l%m " plane we get:" } newline newline {bold V}_pq = iint csub {%l%m} {bold J}_p(%l,%m){bold B(%l,%m)} over {%n(%l,%m)} {bold J}^{%dagger}_q(%l,%m)d%l d%m newline newline

---
Image-plane vs. uv-plane
size 24 { {bold J}_p " is composed of multiple effects: " {bold J}_p = {bold J}_pn {bold J}_{pn-1} ... {bold J}_p1} newline size 24 { ( {bold J}_pn " is \"in the receiver\", " {bold J}_p1 " is \"in the sky\"." )} newline size 24 { "Some " {bold J}"'s do not vary with " %l,%m " -- call them " ital "uv-plane effects." } newline alignr size 24 { "e.g. receiver gain, leakage." } newline size 24 { "Some " {bold J}"'s do vary with " %l,%m " -- call them " ital "image-plane effects." } newline alignr size 24 { "e.g. " bold K ", beam gain, ionosphere" } newline size 24 {"Let's rewrite the " {bold J}_p " product as: " } newline size 24 { {bold J}_p = {{bold J}_pn ... {bold J}_{pk+1}} overbrace {"uv-plane only"} underbrace {{bold G}_p} {bold K}_p {{bold J}_{pk-1} ... {bold J}_p1} overbrace {"uv- & image-plane"} underbrace {{bold E}_p(%l,%m)} } newline size 24 { "Or in other words, " {bold J}_p(%l,%m) = {bold G}_p {bold K}_p(%l,%m) {bold E}_p(%l,%m) } newline size 24 { ("and depending on our particular M.E., " bold G " or " bold E " may be " equiv bold 1) }

---
And Back To The ME....
{bold V}_pq = iint csub {%l%m} {bold J}_p(%l,%m){bold B(%l,%m)} over {%n(%l,%m)} {bold J}^{%dagger}_q(%l,%m)d%l d%m newline newline size 24 { "then becomes: "} newline newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold K}_p {bold E}_p bold B over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 { "(with everything under the " iint " being a function of " %l,%m ")" }

---
The Fourier Transform
size 24 { "and now expanding the " bold K " terms:"} newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({bold E}_p bold B over %n {bold E}^{%dagger}_q) e^{-{2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 { "for narrow fields " %n toward 1 "(and for coplanar arrays " w=0 "), so:"} newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({{bold E}_p bold B {bold E}^{%dagger}_q} underbrace "\"apparent sky\"") {e^{-{2%pi%i}(u_pq%l+v_pq%m)}} underbrace "F.T. kernel" d%l d%m right ) {bold G}^{%dagger}_q
The integral then becomes a 2D Fourier transform of the “apparent sky”.

---
The Fly In The Ointment
{bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({bold E}_p {bold B}over %n {bold E}^{%dagger}_q)e^{{-2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m right ) {bold G}^{%dagger}_q
In the general case, the exponent is not quite an F.T. kernel.
Let's collect the n-terms into an “N-Jones”, and define an “apparent projected sky”:
{bold B}_pq = {bold %N}_p {bold E}_p bold B {bold E}^{%dagger}_q {bold %N}^{%dagger}_q = {bold %N}_pq {bold E}_p bold B {bold E}^{%dagger}_q newline size 24 { " where " {bold %N}_p = 1 over sqrt %n e^{-2%pi%i%w_p(%n-1)}, ~ {bold %N}_pq = {bold %N}_p {bold %N}^%dagger_q } newline size 24 { "(for narrow fields and/or coplanar arrays, " {bold %N}_p toward 1 ")" }

---
Apparent Skies & Apparent Cohaerencies
size 24 {"We now have: "} newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold B}_pq e^{-{2%pi%i}(u_pq%l+v_pq%m)} d%l d%m right ) {bold G}^{%dagger}_q = {bold G}_p {bold X}_pq {bold G}^{%dagger}_q, newline size 24 { "where " {bold X}_pq = size 36 %fcall ( {bold B}_pq ) = size 36 %fcall ( %N_p {bold E}_p bold B {bold E}^%dagger_q %N^%dagger_q ) }
In other words, each antenna pair p-q measures an apparent cohaerency distribution Xpq(u,v) that corresponds to a 2D Fourier Transform of its own apparent projected sky Bpq.
...at a single point in time!

---
Time Is Not On Our Side
Cohaerencies are sampled along a “uv track” over some period of time:
{bold V}_pq(t) = {bold G}_p(t) {bold X}_pq(t,u(t),v(t)) {bold G}^{%dagger}_q(t)
The true sky B is probably constant(?) in time
Image-plane effects (beam shapes, ionosphere) may vary in time, and across the array.
For wide fields, the N term is non-negligible. It varies with w which varies with time.
All this is especially relevant with new telescope designs.

---
The “Classic” Assumptions
size 24 {"The full-sky ME: " } {bold V}_pq = {bold G}_p {bold X}_pq {bold G}^{%dagger}_q, newline size 24 { "where " {bold X}_pq = size 36 %fcall({bold B}_pq), ~{bold B}_pq = {bold %N}_p {bold E}_p bold B {bold E}^{%dagger}_q {bold %N}^%dagger_p }newline newline size 24 { "If we assume that " {bold B}(t) equiv {bold B}, " and "{bold E}_p(t) equiv {bold E}_p equiv bold E, " and " {bold %N}_p toward 1, } newline size 24 "then all baselines will see the same, constant apparent sky: " newline {bold B}_{pq}(t) = bold E bold B {bold E}^%dagger equiv {bold tilde B} newline size 24 "and the array will sample one apparent cohaerency plane: " newline {bold X}_pq(t,u,v) equiv {bold X}(u,v)
Only under these assumptions can we consider an F.T. of the sky as being an accurate representation of what an interferometer sees.

---
Conclusions
Under the “classic” assumptions, the visibilities measured by an array correspond to ONE cohaerency distribution X that is in an F.T. relationship with ONE apparent sky.
In the presence of non-trivial image plane effects, and/or with wide fields and noncoplanar arrays, each interferometer p-q measures its “own” cohaerency Xpq(t), corresponding to its “own” apparent sky Bpq(t) -- variable in time!
The K term becomes an F.T. kernel with narrow FOVs/coplanar arrays, but is “not quite” an F.T. otherwise.

---
Implications?
For calibration, we need to predict & subtract bright sources accurately in the presence of image-plane effects
The M.E. provides all the mathematical apparatus to do this right:
  - remember 3C343
  - remember the ionosphere
The residuals may still need to be corrected...

---
Can We Correct Visibilities?
In general, no...
uv-plane effects (the Gs) can be taken out by simple matrix inversion/multiplication
Image-plane effects correspond to convolution in the uv-plane:
alignl size 24 { {bold V}_pq =size 36 %fcall({bold E}_p{bold B}{bold E}^{%dagger}_q) = size 36 %fcall({bold E}_p) circ size 36 %fcall({bold B}) circ size 36 %fcall({bold E}^{%dagger}_q)}
  - ...with time-variable kernels
  - ...and with each baseline's uv-plane sampled along just a single track
(Note: Bhatnagar et al. (EVLA Memo 100) suggest a method for approximate correction during the imaging step. We'll return to this later.)

---
Correcting At
A Single Point
alignl size 24 { "But we can correct for a single point " %l_0,%m_0: } newline {bold V}'_pq = {bold Z}_p(%l_0,%m_0)^{-1} {bold V}_pq{bold Z}^{-1}_q(%l_0,%m_0)^%dagger "=" newline alignc "=" size 36 %fcall left (({bold Z}_p(%l_0,%m_0))^{-1}{bold Z}_p {bold B} {bold Z}_q^%dagger({bold Z}^{%dagger}_q(%l_0,%m_0))^{-1} right ) newline alignc "=" size 36 %fcall({bold B}') newline newline alignl size 24 { "where " {bold B}'(%l_0,%m_0) = {bold B}(%l_0,%m_0)," but diverges further away." }
In general, uv-data can only be “corrected” for a single point on the sky.
Hence, e.g., multifacet imaging.

---
Playing With The ME
For Fun & Profit

---
Meet Supersim
cd Workshop2008/Day5
Start the browser and load up supersim.py
This is a Siamese script with enough bells and whistles to demonstrate most aspects of wide-field imaging

---
Exercise: The w-effect
To see the effect of the w-term:
  - disable all Jones matrices
  - make a 3x3 grid of sources with grid step 60'
  - make an image (2048 pixels)
size 24 {"Our ME here is:" } newline size 24 { {bold V}_pq = iint csub {%l%m} {{{bold B}over %n} e^{{-2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m} } newline newline size 24 {"...while the imager inverts this ME:" } newline size 24 { {bold V}_pq = iint csub {%l%m} {{bold B} e^{{-2%pi%i}(u_pq%l+v_pq%m)} d%l d%m} } newline

---
Exercise: Beams & Instrumental Polarization
Set grid step to 20'
Enable the E-Jones
  - set beam eccentricity to .1
Open an inspector for E
Make IQUV map (average all channels)
Enable P-Jones
Make another IQUV map.

---
Exercise: Pointing Errors
Enable pointing errors (see the submenu for E-Jones)
  - set to periodic error of 5”
Open inspector for E and for dlm
Make an I map (average all channels)
Observe the difference (or lack thereof...)

---
So What's The Difference?
It's hard to see all that much in the map
(although you could make another map without pointing error, and subtract it...)
So let's build a differential sim instead, to compute the difference between visibliites with and without pointing errors
Set “simulation mode” to “subtract for MS”, for input column use CORRECTED_DATA, for output use MODEL_DATA.
Make an I map.

---
Differential Trees
(Or Simulations About Simulations)
Given infinite CPUs, we can implement m.e.'s of arbitrary precision.
In real life, we have to take shortcuts
(e.g. choosing time/freq intervals here).
The main question: how much error does a particular shortcut introduce?
  - given infinite mathematical skill, we could work it out analytically...
  - ...but given MeqTrees, we don't have to.

---
Exercise: N-correction
With wide fields, it is difficult to distinguish distortion introduced by the w-effect from other distortions
The “Ncorr-Jones” adds an artifical Jones term of:
This causes the sources to image perfectly
Alternative (slow): enable w-correction in the imager (use 1024 convolution funcs)
size 24 { {bold N}_p = 1 over sqrt{%n} e^{{2%pi%i}w_p(%n-1)} }

---
And Now For Something Completely Different:
Time & Bandwidth Smearing
alignl size 24 { "Recall: antennas " p,q " measure: " {vec v}_p = {bold J}_p vec e, ~~ {vec v}_q = {bold J}_q vec e } newline alignl size 24 { "where " {bold J}_p,{bold J}_q " are Jones matrices describing the signal paths"} newline alignl size 24 { "from the source to the antennas." } newline size 24 { "Then " {bold V}_pq = langle ({bold J}_p vec e ) ({bold J}_q vec e)^%dagger rangle = langle {bold J}_p (vec e {vec e}^{%dagger} ) {bold J}_q^%dagger rangle = {bold J}_p langle vec e {vec e}^{%dagger} rangle {bold J}_q^%dagger } newline size 20 { "(making use of " (bold AB)^%dagger = {bold B}^%dagger{bold A}^%dagger ", and " underline "assuming" ~ {bold J}_p " is constant over " langle rangle ")" } newline size 24 { "The inner quantity is known as the " ital "source coherency" ":" } newline size 24 { bold B = langle vec e {vec e}^%dagger rangle = 1 over 2 left ( matrix {I+Q # U+-%i V ## U-+%i V # I-Q } right ) ~ %lrarrow ~ (I,Q,U,V) } newline size 24 { "which we can also call the " italic "source brightness." " Thus:" } newline {bold V}_pq = {bold J}_p bold B {bold J}^{%dagger}_q

---
And Now For Something Completely Different:
Time & Bandwidth Smearing
size 24 { "When deriving the ME, we assumed: " langle {bold J}_p (vec e {vec e}^{%dagger} ) {bold J}_q^%dagger rangle = {bold J}_p langle vec e {vec e}^{%dagger} rangle {bold J}_q^%dagger } newline alignl size 24 { "In effect, we've been computing " {bold V}_pq(t_0,%nu_0), " and assuming "} newline alignl size 24 { "that this close enough to the " ital "vector average" " over " %DELTA t,%DELTA%nu . } newline alignl size 24 { "This is OK as long as " {bold J}_p"s are sufficiently constant over " %DELTA t,%DELTA%nu .} newline alignl size 24 { "But as a minumum, " {bold J}_p " contains " {bold K}_p, "and :" } newline size 24 { {bold K}_p{bold K}^%dagger_q = exp({2%pi%i%nu} over c(u%l+v%m+w(%n-1)))} newline alignr size 20 { (uvw"'s change with " t, " faster for longer baselines") } newline alignl size 24 { "So even in the absence of any additional effects, " } newline size 24 { langle {bold K}_p bold B {bold K}^%dagger_q rangle_{%DELTA t,%DELTA%nu} ~ <> ~ {bold K}_p(t_0,%nu_0) bold B {bold K}^%dagger_q(t_0,%nu_0) } newline alignl size 24 { "This is usually known as time and bandwidth smearing." } newline alignl size 24 { "The effect goes up with " %DELTA t,%DELTA%nu,%l,%m, " and baseline length." }

---
Simulating Smearing
The same effect occurs with other Jones terms, such as ionospheric or tropospheric phase, etc. (hence, decohaerency time).
How to simulate?
The brute force approach:
alignl size 24 { "- Divide each " %DELTA t,%DELTA%nu " into " N times M " sub-intervals, and use" } newline size 24 {langle {bold V}_pq rangle_{%DELTA t,%DELTA%nu} approx 1 over NM sum csub {i,j} {bold V}_pq(t_i,%nu_j)}
Enable resampling in supersim.py (use 5x5) and observe the results...

---
Exercise: Smearing
Set grid step to 30'
Disable all Jones terms
Enable resampling (use 5x5 factors)
Make I map (average all channels)
Optional: try this with the ionosphere, etc.

---
Divide And Conquer
size 24 { {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold K}_p {bold E}_p bold B over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q } newline newline alignc size 24 { "This is linear over " bold B", so if the sky is a sum of sources:" } newline {bold B}(%l,%m) = sum_s {bold B}_s(%l,%m), newline size 24 "then" newline newline {bold V}_pq = {bold G}_p left ( sum csub s iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_s over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 {"And for some sources we can work out the integral exactly."}

---
A Sky Of Point Sources
size 24 {"For a point source " s " of flux " {bold B}_0s=1 over 2 left ( matrix{I_s+Q_s # U_s+%i V_s ## U_s-%i V_s # I_s-Q_s} right ) } newline size 24 { "the "bold B " distribution is a delta-function:"} newline size 24 { {bold B}_s(vec %sigma) = { bold B}_0s%delta(vec %sigma-vec %sigma_s), " or"} newline size 24 { {bold B}_s(%l,%m) = { bold B}_0s%n_s%delta(%l-%l_s,%m-%m_s)~~~ "(do note the " n ")"} newline newline size 24 {"So for a sky of point sources:"} newline {bold V}_pq = {bold G}_p left ( sum csub s {bold K}_ps {bold E}_{ps} {bold B}_0s {bold E}^{%dagger}_{qs} {bold K}^{%dagger}_{qs} right ) {bold G}^{%dagger}_q, newline size 24 { "where " {bold K}_ps = {bold K}_p(%l_s,%m_s), " and "{bold E}_ps = {bold E}_p(%l_s,%m_s). }

---
Extended Sources & Patches
Any B that is not a delta-function gets interesting, especially if E is not trivial, and especially for wider fields (the “not quite an F.T.” problem.)
...but we need to solve this for two reasons.
Reason 1: spatially extended sources...
Reason 2: it is impractical to directly predict large numbers of fainter sources individually, so we need to organize them into “patches”, and find a faster way to predict a patch en masse.

---
First, Reduce To Center...
alignl size 24 {"Consider a source centered on direction " vec %sigma_0 ~~ (%l_0,%m_0), } newline alignl size 24 {"with the phase center at " vec %sigma=0. } newline size 24 { {bold V}_pq = int csub{"sky"} {bold K}_p(vec%sigma) {bold E}_p(vec%sigma) bold B(vec%sigma) {bold E}^{%dagger}_q(vec%sigma) {bold K}^{%dagger}_q(vec%sigma) d%OMEGA = ""} newline size 24 { "Let's integrate in the coordinate system " vec %sigma'=vec%sigma+vec%sigma_0, } newline size 24 { "and define " {bold tilde B}(vec%sigma) equiv {bold B}(vec%sigma+vec%sigma_0), ~{bold tilde E}_p(vec%sigma) equiv {bold B}(vec%sigma+vec%sigma_0): } newline size 24 { {bold V}_pq = int csub{"sky"} {bold K}_p(vec%sigma+vec%sigma_0) {bold E}_p(vec%sigma+vec%sigma_0) bold B(vec%sigma+vec%sigma_0) {bold E}^{%dagger}_q(vec%sigma+vec%sigma_0) {bold K}^{%dagger}_q(vec%sigma+vec%sigma_0) d%OMEGA' = ""} newline size 24 { "" = {bold K}_p(vec %sigma_0) left ( int csub{"sky"} {bold K}_p(vec%sigma) {bold tilde E}_p(vec%sigma) bold tilde B(vec%sigma) {bold tilde E}^{%dagger}_q(vec%sigma) {bold K}^{%dagger}_q(vec%sigma) d%OMEGA right ) {bold K}^%dagger_q(vec %sigma_0) = ""} newline size 24 { "" = {bold K}_p(%l_0,%m_0) left ( iint csub{%l%m} {bold K}_p {bold tilde E}_p bold tilde B over %n {bold tilde E}^%dagger_q {bold K}^%dagger_q d%l d%m right ) {bold K}^%dagger_q(%l_0,%m_0) } newline

---
...Where Life Gets Easier
{bold V}_pq = {bold K}_p0 left ( iint csub{%l%m} {bold K}_p {bold tilde E}_p bold tilde B over %n {bold tilde E}^%dagger_q {bold K}^%dagger_q d%l d%m right ) {bold K}^%dagger_q0
In other words, to predict a source at l0,m0, it is sufficient to predict it at the phase center (shifting E accordingly...), then apply the phase terms Kp0, Kq0 to “move” the source to its true position.
This is beautifully symmetric w.r.t. the ME for a point source:
{bold K}_p0 {bold E}_p0 {bold B}_0 {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0

---
So All We Need
To Figure Out Now...
...is how to predict extended sources at the phase center. We've simplified the problem considerably. If we now expand the K terms:
size 24 { {bold V}_pq = iint csub {%l%m} ({bold E}_p bold B over %n {bold E}^{%dagger}_q) e^{-{2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m } newline size 24 { "When " %n toward 1 ", this becomes a Fourier Transform:"} newline size 24 { {bold V}_pq = iint csub {%l%m} ({{bold E}_p bold B {bold E}^{%dagger}_q} underbrace "\"apparent sky\"") {e^{-{2%pi%i}(u_pq%l+v_pq%m)}} underbrace "F.T. kernel" d%l d%m }
...and we only require the “Weak Assumption” that n→1 over the extent of the source.

---
Or Even More Optimistically...
alignl size 24 { "If we also make the \"Strong Assumption\" that " } newline alignl size 24 { {bold E}_p approx {bold E}_p(0,0) " over the source, then " } newline {bold V}_pq = {bold K}_p0 {bold E}_p0 size 36 %fcall ( {bold B}_0 ) {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
This is very good from a practical point of view, since:
F.T.'s are easier than strange integrals
phase shifts and (in the optimistic case) image-plane effects are applied in the same way to all kinds of sources
we only need to worry about predicting the source (or patch) at the phase center

---
The Bad News
This is only an approximation.
Error levels will depend on:
source flux (in a linear way, so we can talk about relative error);
patch/source size (because of the n term);
the variation in E over the extent of the patch.
We need to develop some feeling for how small the patches/sources need to be to make the error suitably small.
We can build some trees to simulate these errors (well this is actually good news, isn't it?)

---
The Bhatnagar Approach:
Coming Soon To a Tree Near You?
size 48 %fcall ( {bold E}_p{bold B}{bold E}^%dagger_q ) = size 48 %fcall ( {bold E}_p) circ bold X circ size 48 %fcall ({bold E}^%dagger_q ) newline size 24 {"If " {bold E}_p " is sufficiently smooth, then " size 36 %fcall ({bold E}_p) " can be approximated " } newline size 24 {"with just a few low-order Fourier coefficients." }
Convolution with a “small” kernel can be computed directly, fairly cheaply.
...and in fact the interpolation function used in the traditional FFT/gridding method to interpolate X to a given uv track is a form of convolution.
So we can apply E's during gridding, via a suitable modification to the convolution function.
(NB: the inverse process, for N, is w-projection)

---
And That's All, Folks!