Some Announcements
Wednesday bridge and Friday football is on, just like the previous week
  - think about it, we'll do a head count later
Previous days' exercise solutions now linked on the wiki.

---
ME3: Calibration & Correction
Objectives:
Figuring out what calibration is!
Framing the calibration problem in Measurement Equation terms.
Implementing some calibration trees.
svn up Workshop2007 please!

---
What Is Calibration?
...according to Google
# The process whereby the magnitude of the output of a measuring instrument is related to the magnitude of the input force driving the instrument (ie Adjusting a weight scale to zero when there is nothing on it). (Course Material/Ultrasonics/CalibrationMeth/calibrationmethods.htm)
www.ndt-ed.org/GeneralResources/Glossary/letter/c.htm
# The process of adjusting an instrument or compiling a deviation chart so that its reading can be correlated to the actual value being measured.
www.omega.com/literature/transactions/volume1/glossary.html
# The process of choosing attribute values and computational parameters so that a model properly represents the real-world situation being analyzed. For example, in pathfinding and allocation, calibration generally refers to assigning or calculating appropriate values to be entered in impedance and demand items.
www.geog.leeds.ac.uk/staff/m.blake/magis/glossary/esriglos.htm
# (cal·i·bra·tion) (kal²[ibreve]-bra¢sh[schwa]n) 1. determination of the accuracy of an instrument, usually by measurement of its variation from a standard, to ascertain necessary correction factors. 2. measurement of the caliber of a tube.
www.mercksource.com/pp/us/cns/cns_hl_dorlands.jspzQzpgzEzzSzppdocszSzuszSzcommonzSzdorlandszSzdorlandzSzdmd_c_03zPzhtm
# Checking, adjusting and systematically standardizing the graduations of a device.
www.inkcartridgesworld.com/_glossary.html
# The process of establishing a set of values for correct operation.
www.blazepoint.co.uk/faq_label_printers_glossary.html
# A process that establishes, under specified conditions, the relationship between the values indicated by the measuring system, and the corresponding values of a quantity realised by a reference standard or working standard.
www.nzelectricity.co.nz/H9glossary.htm
# process of comparing an instrument's accuracy to known standards
www.tsgc.utexas.edu/stars/glossary1.html
# is defined as the process of quantitatively defining the system response to known, controlled signal inputs.
www.eumetsat.int/en/dps/helpdesk/glossary.html

---
...according to Noordam

---
...according to the
EoR KSG
EoR Signature???

---
Our Definition For Today...
Determining the properties of the sky and the instrument with sufficient accuracy.
“Taking out” (as much as possible) instrumental corruptions.
Subtracting known sources
...to find the noise (or at least to achieve our scientific objectives)

---
“Classic” Calibration
(for phases/gains)
alignl size 24 { "Assume this m.e.: " v_{pq} = g_p size 36 %fcall(b) g^%star_q } newline newline alignl size 24 {"1. Start with a model for the sky brightness, " M(%l,%m)} newline alignl size 24 {"2. F.T. that into model coherencies: " x(u,v) = size 36 %fcall(M) } newline alignl size 24 {"3. Predict 'corrupted' model: " x'_pq = g_p x_{pq}g^%star_q } newline alignl size 24 {"4. Find " g_p "s by fitting " x'_{pq} " to observed " v_{pq} } newline alignl size 24 {"5. Compute corrected visibilities: " v'_{pq} = g^{-1}_p v_{pq}(g^{-1}_q)^%star } newline newline alignl size 24 {"The \"corrected\" visibilities are then in an F.T. relationship " } newline alignl size 24 {"with the true sky " b: ~~~ v'_pq = size 36 %fcall(b) } newline

---
The M.E. Analogue
alignl size 24 { "Assume this m.e.: " {bold V}_{pq} = {bold G}_p size 36 %fcall(bold B) {bold G}^%dagger_q } newline newline alignl size 24 {"1. Start with a model for the sky brightness, " {bold M}(%l,%m)} newline alignl size 24 {"2. F.T. that into model visibilities: " bold X = size 36 %fcall(bold M) } newline alignl size 24 {"3. Predict 'corrupted' model: " {bold X}'_pq = {bold G}_p {bold X}_{pq}{bold G}^%dagger_q } newline alignl size 24 {"4. Find " {bold G}_p "s by fitting " {bold X}'_{pq} " to observed " {bold V}_{pq} } newline alignl size 24 {"5. Compute corrected visibilities: " {bold V}'_{pq} = {bold G}^{-1}_p {bold V}_{pq}({bold G}^{-1}_q)^%dagger } newline alignr size 24 { " (note that " ({bold G}^%dagger)^{-1} = ({bold G}^{-1})^%dagger ")" } newline newline alignl size 24 {"We then again have " {bold V}'_pq = size 36 %fcall(bold B) } newline

---
Or In Broad Terms...
Predict corrupted visibilities
  - we covered this last week
Fit to observed visibilities
  - solving for parameters of the sky and/or the instrument
(Optional: subtract bright sources)
Correct
Rinse & repeat
  - aka the “major loop”: source extraction, updating sky model, etc.

---
Applying Corrections
With MeqTrees
The Meq.MatrixInvert22 node inverts 2x2 matrices.
  - (generalized inversion not yet available)
A Meq.Spigot reads data from the MS.
See ME3/demo1-correct-gains.py.
Re-run ME1 exercise 1 to simulate an MS with instrumental polarization
    - (but fix ap=p*1e-10)
Run ME3/demo1 on this MS, write to the CORRECTED_DATA column, make an IQUV channel map of this column.

---
Exercise 1: Correcting For Parallactic Angle
Re-run ME1 exercise 2 to produce an MS with instrumental polarization and alt-az mounts
(fix ap=p*1e-10)
Make an per-channel IQUV map of the DATA column
Modify ME3/demo1 to correct for P.A. as well
Write corrections to CORRECTED_DATA
Make an IQUV channel map of the CORRECTED_DATA column
Did you get the original, uncorrupted point source back? (I=1 Jy, Q=.2 Jy, U=V=0)

---
Correcting For Multiple Jones Terms
alignl size 24 { "Given an m.e. of the form:" } newline size 24 { {bold V}_pq = {bold J}_pn ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {bold J}^{%dagger}_qn } newline alignl size 24 { "the corrections need to be applied in reverse order:" } newline size 24 { {bold V}'_pq = {bold J}^{-1}_p1 ... {bold J}^{-1}_pn {bold V}_pq ({bold J}^{-1}_qn)^%dagger ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold J}^{-1}_p1 ... {{bold J}^{-1}_pn {bold J}_pn} underbrace {""=1} ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {{bold J}^{%dagger}_qn ({bold J}^{-1}_qn)^%dagger}underbrace{""=1} ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold X}_pq = size 36 %fcall(bold B) } newline newline alignl size 24 {"...and all matrix (non-)commutation rules apply." }

---
So, Is There Always Such A Beast As “Corrected” uv-Data?
alignl size 24 { "Say we now have some image-plane effects:" } newline {bold V}_pq={bold G}_p size 48 %fcall(%N_p {bold E}_p{bold B}{bold E}^{%dagger}_q %N^%dagger_q ){bold G}^{%dagger}_q newline alignl size 24 { "... and we know all of the " {bold G}_p, {bold E}_p, "and (of course) " %N_{p}"'s";} newline alignl size 24 { "then is there a way to obtain \"corrected\" visibilities " {bold V'} } newline size 24 { "such that " } {bold V'}_pq=size 48 %fcall({bold B})~~ ??? newline newline size 24 { " (or at the very least " {bold V'}_pq=size 36 %fcall(%N_p {bold B} %N^%dagger_q) ") ???" } newline

---
Exercise 2:
Ionospheric Corrections
Take our old ME2/demo-30-190.MS
  - re-run ME2/example6-iono.py to corrupt for ionosphere
  - make an image to verify corruptions
Make a script to take the ionosphere back out, write results to the CORRECTED_DATA column.
Make a per-channel map, then a movie.

---
And The Answer Is...
In general, NO!
uv-plane effects (the Gs) can be taken out.
Image-plane effects correspond to convolution in the uv-plane:
alignl size 24 { {bold V}_pq =size 36 %fcall(%N_p{bold E}_p{bold B}{bold E}^{%dagger}_q%N^%dagger_q) = size 36 %fcall({bold E}_p) circ size 36 %fcall(%N_p{bold B}N^%dagger_q) circ size 36 %fcall({bold E}^{%dagger}_q)}
  - ...with time-variable kernels
  - ...and with each baseline's uv-plane sampled along just a single track
(Note: Bhatnagar et al. (EVLA Memo 100) suggest a method for approximate correction during the imaging step. We'll return to this later.)

---
Correcting At
A Single Point
alignl size 24 { "But we can correct for a single point " %l_0,%m_0: } newline bold V' = {bold E}_p(%l_0,%m_0)^{-1} bold V{bold E}^{-1}_q(%l_0,%m_0)^%dagger "=" newline alignc "=" size 48 %fcall left (({bold E}_p(%l_0,%m_0))^{-1}{bold E}_p %N_p bold B %N^%dagger_q {bold E}_q^%dagger({bold E}^{%dagger}_q(%l_0,%m_0))^{-1} right ) newline alignc "=" size 48 %fcall(%N_p bold B' %N^%dagger_q) newline newline alignl size 24 { "where " {bold B'}(%l_0,%m_0) = {bold B}(%l_0,%m_0)," but diverges further away." }
In general, uv-data can only be “corrected” for a single point on the sky.
This is the motivation for facet imaging.

---
Calibration, Revisited
Predict corrupted visibilities
  - we know this, this is simulation
Fit to observed visibilities
  - solving for parameters of sky and/or instrument
(Optional: subtract bright sources)
Correct
Rinse & repeat
  - aka the “major loop”: source extraction, updating sky model, etc.

---
A General Approach
To Fitting & Solving
A tree evaluating any m(t,) also depends on values of parameters up in the tree. We write this as:
m(t,;a,b,...)
Imagine a “magic” constant node a that returns not one, but two values: a and a+a.
Its parent, f, then returns f(a) and f(a+a)...
...and at the bottom we get m(t,;a) and m(t,;a+a)
size 24 { "From this we can estimate: " } newline size 24 { {%deriv m} over {%deriv a} approx {m(a+%delta a)-m(a)} over {%delta a}, ~~ {%deriv m} over {%deriv b} approx {m(b+%delta b)-m(b)} over {%delta b}} newline size 24 { "And then try to minimize or maximize " m... } newline size 24 { "(Which even a salmon can do.)" } newline

---
Maaijke's Turn:
Introduction To Solving
cd Workshop2007/Solvers
See separate slides in Solving.pdf

---
Exercise 3:
Fitting The Ionosphere
Start with Intro1/example7-iono3.py
Take the tec:2 node, which returns TEC as a function of x,y,t
Make a solver tree:
  - TEC(t;xy) on one side
  - MIM(t;xy) on other side:
  - each ckl(t) should be a polc in time, you solve for its coefficients
  - polynomial order (in time and xy) should be a compile-time option
Play with various polynomials to see how well we can fit the TEC.
size 24 { MIM(t;xy) = sum csub {k,l} c_kl(t)x^k y^l}

---
Calibration Of An MS
A model tree computes corrupted visibilities Xpq(t,)
Spigots return observed data Vpq(t,)
We can take the difference and form up a 2 sum...
...and try to minimize it w.r.t. the solvable parameters.
Which is the same as fitting the model to the data, in a least-squares sense.
We can thus solve for any (reasonable) subset of parameters of a measurement equation.

---
A Real-Life Example: 3C343
Field is dominated by two bright sources:
  - 3C343.1 (~6 Jy) at phase center
  - 3C343 (~1.8 Jy) off-center
Significant polarization
12-hour WSRT observation, 03/08/2000
64 channels ~ 1.2 Ghz (we use 26)
3C343.MS pre-processed by Michiel Brentjens
Pristine copy:
cp -a (/net/birch)/data/oms/Workshop2007/3C343.MS .
(/apps/Timba/data on jop0x)

---
Viewing MSs
See ME3/demo2-view343.py
This is just like our old spigot-sink script from Intro2, but rewritten with Meow
The simplest/quickest kind of MS inspector you can make with MeqTrees, you can use it for any MS...
Load the inspect_spigots bookmark and run the tree.
Make an image of the DATA column.

---
Step 1: Solving For
Source Fluxes
See ME3/demo4-cal343.py, build the tree but do not run it yet
This uses Meow to construct a model with two point sources
Simultaneous solution for two sources
  - note how this is different from peeling
I and Q fluxes are Meq.Parms: i.e. potentially solvable parameters
  - polynomial in frequency

---
 Polynomial Fluxes?
I and Q fluxes are set up with a shape, to make them polynomials of frequency
This accounts for spectral indices, and also beams and instrumental polarization
size 24 {"This is the m.e. we end up with:" } newline size 24 { {bold V}_pq = {bold K}_p1{bold B}_1{bold K}^%dagger_q1 + {bold K}_p2{bold B}_2{bold K}^%dagger_q2; ~~~ {bold B}_s = left ( matrix{I_s+Q_s # 0 ## 0 # I_s-Q_s } right ) } newline size 24 { I_s,Q_s = sum csub k c_k %nu^k }

---
CondEqs and Solvers
Meq.CondEqs form up the difference between two branches
  - predicted and measured
...and estimate derivatives.
A Meq.Solver uses these to run an iterative solution
A separate solution is run for each tile.
The previous tile's solution is used as the starting point for the next tile.

---
Request Sequencing
Once we have a solution, we want to apply it to the data to generate, e.g., corrected data, or residuals
This means we want to execute two branches in strict sequence:
  - first the Solver branch
  - then the correct/subtract/etc. branch
A Meq.ReqSeq executes its two children in sequence, then returns the result of one of the children.

---
Running The Tree...
Set Solver options in TDL Exec menu:
  - Convergence threshold: 0.001
  - Assume balanced equations: false
Load up all bookmarks, set output column to CORRECTED_DATA, and run “test forest” with a tile size of 100.
Observe plots in bookmarks.
We should get I fluxes of 5.5~6 Jy and 1.6~1.8 Jy

---
Solving For Phases
Flux solutions have been written out to a table (3C343.MS/sources.mep)
The next time we use the I and Q Meq.Parms in a tree, they will be initialized from this table.
So now we can try to solve for gain-phases, while keeping fluxes fixed

---
Exercise 4: Solving For Phases
alignl size 20 {"Start with the previous demo, and add some solvable phase terms." } newline alignl size 20 {"The following m.e. should be implemented: "} newline size 24 { {bold V}^{"(predict)"}_pq = {bold G}_p ( {bold K}_p1{bold B}_1{bold K}^%dagger_q1 + {bold K}_p2{bold B}_2{bold K}^%dagger_q2 ) {bold G}^%dagger_q } newline size 24 { {bold G}_p = left ( matrix{ e^{i%phi_px} # 0 ## 0 # e^{i%phi_py} } right ) } newline alignl size 20 { %phi_px,%phi_py " are solvable Meq.Parms of 0-order (i.e. non-polc)," } newline size 20 { "(use 0 for a starting value)" } newline alignl size 20 {"The following correction should be implemented: "} newline size 24 { {bold V}^{"(corr)"}_pq = {bold G}^{-1}_p ({bold V}^{"(obs)"}_pq - {bold V}^{"(predict)"}_pq) ({bold G}^{-1}_q)^%dagger } newline

---
Exercise 4, Continued
Set tile size to 1 (i.e. a separate phase solution for every timeslot)
Adjust some Solver options:
  - Convergence threshold: 1e-6
  - Assume balanced equations: true
Run the tree
Complete MS would take too long, but you can verify correctness by tracking 2, which should get smaller.
Look also at the residual inspector.
If you're ambitious, add an “inspector” for phases.

---
Flagging
Real data has RFI and stuff, always needs flagging
You can flag an MS using your favourite flagger...
  - or MeqTrees itself
3C343.MS already contains some coarse preliminary flags, but from looking at the residuals, they are obviously insufficient

---
Flags On Trees
Data flags are represented by a flags field in the vellset of a result
Load ME3/demo2-view343.py:
  - publish, e.g., spigot:0:1
  - run with a tile size of 100
  - right-click in inspector, select “Show” or “Hide flagged data”.
  - look at snapshot for spigot tile #6
flags is an integer array of (usually) the same shape as value, non-zero indicates “flagged”.

---
Flag Propagation
In MeqTrees
...only usually same shape as value
  - collapsed axes are possible (i.e. 100x1 flags for a 100x32 value, a.k.a. “row flags”)
flags is a bitmask, each bit represents a flag category.
Nodes ignore flagged values by default
  - controlled by flag_mask option, so you can selectively ignore flag categories
Flags automatically propagate from child to parent

---
Flagging On The Fly
Let's implement two simple flagging algorithms:
Obviously, they ought to be applied to residuals...
size 24 { "1. Absolute-value clipping:" } newline size 24 { "flag if " lline v(t,%nu) rline >= v_0 " (for " v " in XX,XY,YX,YY)" } newline newline size 24 { "2. RMS clipping:" } newline size 24 { v_"abs" := lline v rline ~~~ v_"mean" := langle v_"abs" rangle_{t,%nu} ~~~ %DELTA v:=v_"abs" - v_"mean"} newline size 24 { "flag if " lline %DELTA v rline >= n cdot "rms"(%DELTA v) }

---
Making New Flags
All you need is two special nodes:
  - Meq.ZeroFlagger flags its child's value based on a comparison to 0.
  - Meq.MergeFlags merges flags across children.
The child of the ZeroFlagger is called the flag condition. You can make any tree you like for the flag condition!
Flagging becomes a side branch of sorts.

---
Flagging In Action
Load up ME3/demo4-flag343.py
This makes flagging trees for our two algorithms
  - conditional on compile-time options
First make sure “Write flags to output” is not checked.
If “Ignore MS flags” is set, the spigot is created with a flag_mask of 0, thus ignoring initial flags from the MS

---
Flagging In Action, Continued
The two flaggers work in sequence
  - this is usually a good idea, as absolute clipping makes the rms estimate more accurate
  - Meq.StdDev computes the rms w.r.t. the mean value
Use the CORRECTED_DATA column
Experiment with various flag settings and see the effect via the inspectors.
Flags won't be written until “Write flags to output” is checked.

---
Exercise 5:
Flagging The Solution
After a solve, we have residuals in the tree, so we can flag based on residuals on the fly.
Start with the previous calibration script, and insert our two flaggers from demo4 between the residuals and the sinks.
  - also insert inspector, so we can see residuals before and after flagging

---
More Meowing
Most solve trees look similar, and involve a lot of housekeeping.
...which is usually all the same.
Sounds like a job for a framework.
Meow.StdTrees implements a standard solver tree (among other things)
See ME3/example5-meow343.py for a complete example

---
DO Try This At Home
We'll try to do a “complete” calibration
This is a hefty demo, we don't have enough CPU or RAM for all of you to run it simultaneously
I'll run it myself
Please load up and study the tree and script, but don't execute anything.
You can try running it yourself off-line (as long as you don't do it all together...)

---
Using Meow.StdTrees
We form up a predict tree as before
We then create a standard SolveTree based on our predict tree
We give it inputs (the spigots), and we get back outputs (the residuals)
We correct the residuals
...add a few visualizers
And feed the residuals to sinks
Finally, we define some “solve jobs”

---
Managing Parameters,
The Problem
The problem: we use something like Meow to form up trees
These trees will have Meq.Parm nodes in them somewhere, but we don't know what they're called
  - and we shouldn't know – these are implementation details, and they can change
...yet we must pass a list of parameters to the solver so that we can solve for them

---
Managing Parameters,
The Solution
node.search() searches all subtrees above the designated node, and returns a list of nodes matching some criteria.
In this case matching the given tags.
When Meow creates Meq.Parms, it tags them, following a certain convention
predict.search(tags=”flux solvable”)
then returns all solvables related to flux.

---
Why Tags Are Good
At the top level, we don't need to know any details about which Meq.Parms our tree has
...we just need to know the tagging convention
We then have a generic mechanism for finding “interesting” sets of nodes
Useful for other things, too:
  - e.g. generating bookmarks

---
Step 1: Solving For Fluxes (Again)
Note how the “TDL Exec” menu now has separate sub-menus for different kinds of solutions
These are set up by SolveTree.define_solve_job()
Each kind of solution can have its own set of solver options, tiling, etc.
We now clear out the old solutions, and solve for fluxes anew
...over the entire 12 hours (just because we can!)

---
Step 2: Phases
Fluxes are underestimated (5.3, 1.6 Jy) because phases are unaligned
We now solve for phases, using the current flux solution
We solve with a tile size of 15, while the phase parameters are subtiled with a size of 1. This makes the solution go faster (and more parallel)
Observe residuals and G inspectors as we go along
Observe map

---
Step 3: Fluxes, redux
We now repeat the flux solution. This time, the tree will pick up the phase solutions obtained in the previous step.
Note that at no stage is the input data corrected. We don't take the phases “out” of the data, we just put them into the predict model.
This time we get higher flux solutions.
Observe map, background is showing up, but there's clear artifacts around our two sources.

---
Step 4: Gains
We can now do a solution for gain-amplitudes, using the current estimates for fluxes and phases.
Observe G inspector.
Observe map – the central source is gone, but there's something left at the position of the off-center source.
Conjecture: the off-center gain varies differently from the on-center gain. Pointing errors?

---
Exercise 6:
Differential Gains
alignl size 20 {"Let's implement this m.e.:" } newline size 24 { {bold V}^{"(predict)"}_pq = {bold G}_p ( {bold K}_p1{bold B}_1{bold K}^%dagger_q1 + {bold E}_p{bold K}_p2{bold B}_2{bold K}^%dagger_q2{bold E}^%dagger_q ) {bold G}^%dagger_q } newline
Start with ME3/example5-meow343.py
Add an E-Jones term for off-center (differential) gain
Solve for G and E amplitudes simultaneously, or for E separately
Observe the E inspector
Try to get rid of 3C343 in the residuals

---
Goodbye 3C343...
By rerunning our flux and G phase solutions, we can completely eliminate both sources
If we want to really get to the noise, we should add the faint background sources to our model
This is essentially the “major cycle”
Sarod has a script for CLEANing an image, and converting the clean components into a model

---
Slightly More
Exotic Calibration
In principle anything in the tree can be a solvable parameter
...and can be attempted to be solved for (given enough data)
Instead of calibrating individual Jones matrix elements, we can make them functions of something else, and calibrate that “something else”
E.g., a Minimum Ionospheric Model

---
Calibrating The Ionosphere
Let's try to calibrate for the simulated ionosphere we produced before
We'll pretend we know the source fluxes and positions
  - this what the LOFAR GSM is for...
We'll pretend we know nothing about the ionosphere, and model it by a flat blanket, with a polynomial TEC distribution
We'll then solve for the coefficients

---
The Gory Details...
alignl size 24 {"Ionospheric phase delay is " {bold Z(T)} = e^{-i50%pi T c over %nu } } newline alignl size 24 {"For TEC, we'll use " T(x,y) = sum csub {k,l} x^k y^l } newline alignl size 24 {"and implement the following m.e.:"} newline size 24 {{bold V}_pq = sum csub s {bold Z}_{ps} {bold V}^{(s)}_{pq} {bold Z}^%dagger_{qs}} newline alignl size 24 {"where the source visibility " {bold V}^{(s)}_pq " comes from the Meow model," } newline alignl size 24 {"and " {bold Z}_ps = {bold Z}(T(x_ps,y_ps)), } newline alignl size 24 {x_ps,y_ps " being the piercing point from station " p " to source " s.}

---
First, Simulate...
We'll use a different MS:
  - 100-103.1 MHz, 10 kHz channels
  - more LOFAResque, and easier to fit phase when it doesn't wrap channel to channel!
We'll simulate TIDs in x and y
Starting with zero amplitude at t=0, and gradually increasing
  - This is because we need “phase lock”, which least-squares (usually) struggles with

---
Running The Simulation
You can just copy a pre-fabbed MS from here:
  - cp -a (/net/birch)/data/oms/
      - Workshop2007/demo-lofar.MS .
      - (/apps/Timba/data on jop0x)
I'll demo the simulation step to show what ionosphere we're putting in

---
Running The Solution
Load up ME3/example6-iono-cal.py
(use “Load TDL script” or Ctrl+L)
Set the following options:
  - Grid size: 1, step: 5'
  - Ionospheric model: mim_poly
  - Subtract sources in output
  - MIM options | Polc degree in X/Y: 2
  - MIM options | Polc degree in time: 1
  - MIM options | Base TEC value: 10
Compile and run with a tile size of 2, watch the bookmarks

---
Comments On The Tree
Note how the script is extremely similar to the 3C343 script
  - just a different Jones term
  - that's the power of frameworks
Details of the MIM are hidden inside mims.py, we could in principle add other models there
MIM parameters are found through node.search()

---
Ionospheres Are Hard...
This is obviously a hard problem for a least-squares solver
  - and our model is not the best
  - although it fits better if we bump up the polynomial order
  - though not always...
Other approaches needed...
  - orthogonal polynomials
  - non-parametric models, subspace decomposition?
  - Solvers based on Kalman-type filters