ME3: Extended Sources,
Images, Image-Plane Effects
Objectives:

---
Is There Such a Thing As “Corrected” uv Data?
alignl size 24 { "Say we have a set of \"corrupted\" visibilities:" } newline {bold V}_pq={bold G}_p size 48 %fcall(%N_pq {bold E}_p{bold B}{bold E}^{%dagger}_q){bold G}^{%dagger}_q newline alignl size 24 { "... and we know all of the " {bold G}_p, {bold E}_p, "and (of course) " %N_{pq};} newline alignl size 24 { "then is there a way to obtain \"corrected\" visibilities " {bold V'} } newline size 24 { "such that " } {bold V'}_pq=size 48 %fcall({bold B}) newline newline size 24 { " (or at the very least " {bold V'}_pq=size 36 %fcall(%N_pq {bold B}) ") ???" } newline

---
NO!
uv-plane effects (the Gs) can be easily taken out:
alignl size 24 { "if " {bold V} = {bold G}_p size 36 %fcall({bold tilde B}) {bold G}^{%dagger}_q, " and we know " bold G,} newline alignl size 24 { "then we can derive " {bold V'} = {bold G}^{-1}_p {bold V} ({bold G}^{%dagger}_q)^-1 equiv size 36 %fcall({bold tilde B}) }.
image-plane effects are generally irreversible:
alignl size 24 { bold V =size 36 %fcall(%N_pq{bold E}_p{bold B}{bold E}^{%dagger}_q) = size 36 %fcall(%N_pq) circ size 36 %fcall({bold E}_p) circ size 36 %fcall({bold B}) circ size 36 %fcall({bold E}^{%dagger}_q) } newline alignl size 24 { "since convolution is, in general, irreversible." }

---
Correcting at a single point
alignl size 24 { "But we can correct for a single point " %l_0,%m_0: } newline bold V' = {bold E}_p(%l_0,%m_0)^{-1}%N_pq(n_0)^{-1}bold V{bold E}^{%dagger}_q(%l_0,%m_0)^-1 "=" newline alignc "=" size 48 %fcall left (({bold E}_p(%l_0,%m_0))^{-1}%N_pq(%n_0)^{-1} %N_pq {bold E}_p bold B {bold E}_q^%dagger({bold E}^{%dagger}_q(%l_0,%m_0))^{-1} right ) newline alignc "=" size 48 %fcall(bold B') newline newline alignl size 24 { "where " {bold B'}(%l_0,%m_0) = {bold B}(%l_0,%m_0)," but diverges further away." }
In general, uv data can only be “corrected” for a single point on the sky.
This is the motivation for facet imaging.
(There are some shortcuts...)

---
Divide & Conquer
This is fine in theory, but in practice the general integral form of the ME is computationally intractable. Shortcuts needed!
alignl size 24 { "(Let's ignore the " bold G " terms for now, since they're trivial to add.)" } newline {bold V}_pq = iint csub {%l%m} {bold K}_p {bold E}_p bold B {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m newline size 24 { "then if " bold B " is a sum of sources (patches) " bold B = sum csub s {bold B}_s, } newline {bold V}_pq = sum csub s {bold V}^{(s)}_{pq} = sum csub s iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_s {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m newline size 24 { "and we can consider the ME for each kind of source individually." }

---
Case 1. Point Sources
Point sources are trivial, since their B is a delta function.
size 24 { {bold V}_pq = iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_0 %delta(size 24{%l-%l_0,%m-%m_0}) {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m ~ = "" } newline size 24 { alignc "" = ~ {bold K}_p(size 24{%l_0,%m_0}) {bold E}_p(size 24{%l_0,%m_0}) {bold B}_0 {bold E}^{%dagger}_q(size 24{%l_0,%m_0}) {bold K}^{%dagger}_q(size 24{%l_0,%m_0}) } ~= "" newline newline alignc "" = ~ {bold K}_p0 {bold E}_p0 {bold B}_0 {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
Product of five 2x2 matrices.
We can predict point sources perfectly.
Computationally practical for a limited number of sources.

---
Case 2. Extended Sources
And Patches
Any B that is not a delta-function gets interesting, especially if E is not trivial, and especially for wider fields (the “not quite an F.T.” problem.)
...but we need to solve this for two reasons.
Reason 1: spatially extended sources
Reason 2: it is impractical to directly predict large numbers of fainter sources individually, so we need to organize them into “patches”, and find a faster way to predict a patch en masse.

---
What Is a Small Patch?
For the time being, we make no distinction between an extended source and a patch.
alignl size 24 {"By definition, the source (or patch) has limited extent: "} newline size 24 { bold B(%l,%m) toward 0 " outside some \"small\" region " S " centered on " %l_0,%m_0. } newline alignl size 24 { "Now let's assume that " S " is small enough that " } newline size 24 { %n = sqrt(1-%l^2-%m^2) approx %n_0 = sqrt(1-%l^2_0-%m^2_0) " over " S. } newline alignl size 24 {"Let's further assume that " bold E " is almost constant over " S:} newline size 24 { {bold E}_p(%l,%m) approx {bold E}_p(%l_0,%m_0) = {bold E}_p0} newline newline alignr size 20 {"(And if not, we can always split " S " up into smaller regions.)"} newline

---
Reducing to an F.T.
size 24 {"Then: "} newline size 24 { {bold V}_pq approx iint csub {%l%m} ({bold E}_p0 bold B {bold E}^{%dagger}_q0)1 over %n_0 e^{{2%pi%i}over %lambda(u_pq%l+v_pq%m+w_pq(%n_0-1))} d%l d%m = "" } newline size 20 {"(and substituting " %l=(%l-%l_0)+%l_0, %m=(%m-%m_0)+%m_0 " )" } newline size 24 { "" = { 1 over n_0 e^{{2%pi%i}over %lambda(u_pq%l_0+v_pq%m_0+w_pq(%n_0-1))} } underbrace {binom {{bold K}_p(%l_0,%m_0){bold K}^{%dagger}_q(%l_0,m_0),} {"i.e. the phase term at " %l_0,%m_0}} {bold E}_p0 {left ( iint csub {%l%m} bold B e^{{2%pi%i}over %lambda(u_pq(%l-%l_0)+v_pq(%m-%m_0))} d%l d%m right )} underbrace {"The F.T. of " bold B " shifted to " %l=%m=0} {bold E}^{%dagger}_q0 = "" } newline alignc "" = ~ {bold K}_p0 {bold E}_p0 size 48 %fcall ( {bold B}_0 ) {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
In other words, we can approximate the source by doing an F.T. of the source at the phase centre, followed by a phase shift K corresponding to the real source position.

---
The Good News
{bold K}_p0 {bold E}_p0 size 48 %fcall ( {bold B}_0 ) {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
Compare this to the ME for a point source:
{bold K}_p0 {bold E}_p0 {bold B}_0 {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
This is very good from a practical point of view, since:
F.T.'s are cheaper than strange integrals
phase shifts and image-plane effects are applied in the same way to all kinds of sources
we only need to worry about predicting the source (or patch) at the phase center

---
The Bad News
This is only an approximation.
Error levels will depend on:
source flux (linearly, so we can talk about relative error);
patch/source size (because of the n term);
the variation in E over the extent of the patch.
We need to develop some feeling for how small the patches need to be to make the error suitably small.
We can build some trees to simulate these errors (well this is actually good news, isn't it?)