ME3: Calibration & Correction
Objectives:
Figuring out what calibration is!
Framing the calibration problem in Measurement Equation terms.
Implementing some calibration trees.

---
What Is Calibration?
...according to Google
# The process whereby the magnitude of the output of a measuring instrument is related to the magnitude of the input force driving the instrument (ie Adjusting a weight scale to zero when there is nothing on it). (Course Material/Ultrasonics/CalibrationMeth/calibrationmethods.htm)
www.ndt-ed.org/GeneralResources/Glossary/letter/c.htm
# The process of adjusting an instrument or compiling a deviation chart so that its reading can be correlated to the actual value being measured.
www.omega.com/literature/transactions/volume1/glossary.html
# The process of choosing attribute values and computational parameters so that a model properly represents the real-world situation being analyzed. For example, in pathfinding and allocation, calibration generally refers to assigning or calculating appropriate values to be entered in impedance and demand items.
www.geog.leeds.ac.uk/staff/m.blake/magis/glossary/esriglos.htm
# (cal·i·bra·tion) (kal²[ibreve]-bra¢sh[schwa]n) 1. determination of the accuracy of an instrument, usually by measurement of its variation from a standard, to ascertain necessary correction factors. 2. measurement of the caliber of a tube.
www.mercksource.com/pp/us/cns/cns_hl_dorlands.jspzQzpgzEzzSzppdocszSzuszSzcommonzSzdorlandszSzdorlandzSzdmd_c_03zPzhtm
# Checking, adjusting and systematically standardizing the graduations of a device.
www.inkcartridgesworld.com/_glossary.html
# The process of establishing a set of values for correct operation.
www.blazepoint.co.uk/faq_label_printers_glossary.html
# A process that establishes, under specified conditions, the relationship between the values indicated by the measuring system, and the corresponding values of a quantity realised by a reference standard or working standard.
www.nzelectricity.co.nz/H9glossary.htm
# process of comparing an instrument's accuracy to known standards
www.tsgc.utexas.edu/stars/glossary1.html
# is defined as the process of quantitatively defining the system response to known, controlled signal inputs.
www.eumetsat.int/en/dps/helpdesk/glossary.html

---
...according to Noordam

---
...according to the
EoR KSG
EoR Signature???

---
Our Definition For Today...
Determining the properties of the sky and the instrument with sufficient accuracy.
“Taking out” (as much as possible) instrumental corruptions.
Subtracting known sources.

---
“Classic” Calibration
(for phases/gains)
alignl size 24 { "Assume this m.e.: " v_{pq} = g_p size 36 %fcall(b) g^%star_q } newline newline alignl size 24 {"1. Start with a model for the sky brightness, " M(%l,%m)} newline alignl size 24 {"2. F.T. that into model coherencies: " x(u,v) = size 36 %fcall(M) } newline alignl size 24 {"3. Predict 'corrupted' model: " x'_pq = g_p x_{pq}g^%star_q } newline alignl size 24 {"4. Find " g_p "s by fitting " x'_{pq} " to observed " v_{pq} } newline alignl size 24 {"5. Compute corrected visibilities: " v'_{pq} = g^{-1}_p v_{pq}(g^{-1}_q)^%star } newline newline alignl size 24 {"The \"corrected\" visibilities are then in an F.T. relationship " } newline alignl size 24 {"with the true sky " b: ~~~ v'_pq = size 36 %fcall(b) } newline

---
The M.E. Analogue
alignl size 24 { "Assume this m.e.: " {bold V}_{pq} = {bold G}_p size 36 %fcall(bold B) {bold G}^%dagger_q } newline newline alignl size 24 {"1. Start with a model for the sky brightness, " {bold M}(%l,%m)} newline alignl size 24 {"2. F.T. that into model visibilities: " bold X = size 36 %fcall(bold M) } newline alignl size 24 {"3. Predict 'corrupted' model: " {bold X}'_pq = {bold G}_p {bold X}_{pq}{bold G}^%dagger_q } newline alignl size 24 {"4. Find " {bold G}_p "s by fitting " {bold X}'_{pq} " to observed " {bold V}_{pq} } newline alignl size 24 {"5. Compute corrected visibilities: " {bold V}'_{pq} = {bold G}^{-1}_p {bold V}_{pq}({bold G}^{-1}_q)^%dagger } newline alignr size 24 { " (note that " ({bold G}^%dagger)^{-1} = ({bold G}^{-1})^%dagger ")" } newline newline alignl size 24 {"We then again have " {bold V}'_pq = size 36 %fcall(bold B) } newline

---
Or In Broad Terms, Calibration Is...
Predict corrupted visibilities
  - this is exactly the same problem as simulation
Fit to observed visibilities
  - solving for parameters of sky and/or instrument
(Optional: subtract bright sources)
Correct
Rinse & repeat
  - aka the “major loop”: source extraction, updating sky model, etc.

---
Part I. Corrections
With MeqTrees
The Meq.MatrixInvert22 node inverts 2x2 matrices.
  - (generalized inversion not yet available)
A Meq.Spigot reads data from the MS.
See ME3/demo1-correct-gains.py.
Re-run ME1 exercise 1 to simulate an MS with instrumental polarization.
Run ME3/demo1 on this MS, write to the CORRECTED_DATA column, make an IQUV channel map of this column.

---
Exercise 1: Correcting For Parallactic Angle
Re-run ME1 exercise 2 to produce an MS with instrumental polarization and alt-az mounts
Make an per-channel IQUV map of the DATA column
Modify ME3/demo1 to correct for P.A.
Write corrections to CORRECTED_DATA
Make an IQUV channel map of the CORRECTED_DATA column
Did you get an unpolarized point source back?

---
Correcting For Multiple Jones Terms
alignl size 24 { "Given an m.e. of the form:" } newline size 24 { {bold V}_pq = {bold J}_pn ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {bold J}^{%dagger}_qn } newline alignl size 24 { "the corrections need to be applied in reverse order:" } newline size 24 { {bold V}'_pq = {bold J}^{-1}_p1 ... {bold J}^{-1}_pn {bold V}_pq ({bold J}^{-1}_qn)^%dagger ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold J}^{-1}_p1 ... {{bold J}^{-1}_pn {bold J}_pn} underbrace {""=1} ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {{bold J}^{%dagger}_qn ({bold J}^{-1}_qn)^%dagger}underbrace{""=1} ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold X}_pq = size 36 %fcall(bold B) } newline newline alignl size 24 {"...and all matrix (non-)commutation rules apply." }

---
So, Is There Always Such A Beast As “Corrected” uv-Data?
alignl size 24 { "Say we now have some image-plane effects:" } newline {bold V}_pq={bold G}_p size 48 %fcall(%N_p {bold E}_p{bold B}{bold E}^{%dagger}_q %N^%dagger_q ){bold G}^{%dagger}_q newline alignl size 24 { "... and we know all of the " {bold G}_p, {bold E}_p, "and (of course) " %N_{p}"'s";} newline alignl size 24 { "then is there a way to obtain \"corrected\" visibilities " {bold V'} } newline size 24 { "such that " } {bold V'}_pq=size 48 %fcall({bold B})~~ ??? newline newline size 24 { " (or at the very least " {bold V'}_pq=size 36 %fcall(%N_p {bold B} %N^%dagger_q) ") ???" } newline

---
Exercise 2:
Ionospheric Corrections
Run ME2/demo....... to simulate an MS with ionospheric corruptions.
Extend ME3/demo1 to take the ionosphere back out, write results to the CORRECTED_DATA column.
Make a per-channel map.

---
And The Answer Is...
In general, NO!
uv-plane effects (the Gs) can be taken out.
Image-plane effects correspond to convolution in the uv-plane:
alignl size 24 { {bold V}_pq =size 36 %fcall(%N_p{bold E}_p{bold B}{bold E}^{%dagger}_q%N^%dagger_q) = size 36 %fcall({bold E}_p) circ size 36 %fcall(%N_p{bold B}N^%dagger_q) circ size 36 %fcall({bold E}^{%dagger}_q)}
  - ...with time-variable kernels
  - ...and with each baseline's uv-plane sampled along just a single track
(Note: Bhatnagar et al. (EVLA Memo 100) suggest a method for approximate correction during the imaging step. We'll return to this later.)

---
Correcting At
A Single Point
alignl size 24 { "But we can correct for a single point " %l_0,%m_0: } newline bold V' = {bold E}_p(%l_0,%m_0)^{-1} bold V{bold E}^{-1}_q(%l_0,%m_0)^%dagger "=" newline alignc "=" size 48 %fcall left (({bold E}_p(%l_0,%m_0))^{-1}{bold E}_p %N_p bold B %N^%dagger_q {bold E}_q^%dagger({bold E}^{%dagger}_q(%l_0,%m_0))^{-1} right ) newline alignc "=" size 48 %fcall(%N_p bold B' %N^%dagger_q) newline newline alignl size 24 { "where " {bold B'}(%l_0,%m_0) = {bold B}(%l_0,%m_0)," but diverges further away." }
In general, uv-data can only be “corrected” for a single point on the sky.
This is the motivation for facet imaging.

---
Calibration, Revisited
Predict corrupted visibilities
  - this is exactly the same problem as simulation
Fit to observed visibilities
  - solving for parameters of sky and/or instrument
(Optional: subtract bright sources)
Correct
Rinse & repeat
  - aka the “major loop”: source extraction, updating sky model, etc.

---
A General Approach
To Fitting & Solving
A tree evaluating any m(t,) also depends on values of parameters up in the tree. We write this as:
m(t,;a,b,...)
Imagine a “magic” constant node a that returns not one, but two values: a and a+a.
Its parent, f, then returns f(a) and f(a+a)...
...and at the bottom we get m(t,;a) and m(t,;a+a)
size 24 { "From this we can estimate: " } newline size 24 { {%deriv m} over {%deriv a} approx {m(a+%delta a)-m(a)} over {%delta a}, ~~ {%deriv m} over {%deriv b} approx {m(b+%delta b)-m(b)} over {%delta b}} newline size 24 { "And then try to minimize or maximize " m... } newline size 24 { "(Which even a salmon can do.)" } newline

---
Calibration
A model tree computes corrupted visibilities Xpq(t,)
Spigots return observed data Vpq(t,)
We can take the difference and form up a 2 sum...
...and try to minimize it w.r.t. solvable parameters.
Which is the same as fitting the model to the data, in a least-squares sense.
We can thus solve for any (reasonable) subset of parameters of a measurement equation.

---
...And Not Just Calibration
Floptix: controlling active optics via MeqTrees
  - parameters are actuator positions
  - we manipulate actuators until a test pattern is properly represented.
The m() at the bottom of the tree can be some figure of merit.
  - Minimizing or maximizing m() is then some kind of optimization.
  - e.g. find optimal antenna positions?
Tony's FPA simulations problem.

---
Applying Calibration
alignl size 24 { "Once we have solved for parameters of an ME, correcting " } newline alignl size 24 { "for uv-plane effects is easy: just invert the " {bold G}_p"s," } newline alignl size 24 { "and compute " {bold V}^"(corr)"_pq = {bold G}_p^{-1}{bold V}^"(obs)"_pq ({bold G}_q^{-1})^%dagger . } newline size 20 { "(With multiple Jones matrices, just apply inverse terms in order.)" } newline alignl size 24 { "For image-plane effects this is not an option, as we saw before." } newline alignl size 24 { "We can only correct at a single point. In any case we should " } newline alignl size 24 { "remove all the bright sources, by using the ME solutions to" } newline alignl size 24 { "predict their best-estimate visibilities " {bold V}^(s)_pq .} newline size 24 { {bold V}^"(res)"_pq = {bold J}_p^{-1}left ( {bold V}^"(obs)"_pq - sum csub s {bold V}^(s)_pq right )({bold J}_q^{-1})^%dagger }

---
...And Now In MeqTrees
The MatrixInvert22 node inverts a 2x2 matrix.
The ReqSeq node provides sequencing:
  - first executes one child branch. This contains the Solver, which solves and updates the Parms.
  - then, it executes the second branch, which inverts the best-fit Jones terms and computes the residual visibilities.