ME2: The Full-Sky
Measurement Equation
Objectives:
Extending the M.E. to a full sky
Mapping this onto conventional implicit assumptions, and understanding their limitations
Simulating multiple point sources with image-plane effects (e.g. primary beam)

---
The Full-Sky ME
size 24 { "ME of a single point:" } newline {bold V}_pq = {bold J}_p {bold B} {bold J}^{ %dagger }_q newline size 24 {"The sky has a brightness density: "} {bold B}(vec s) newline size 24 {"(where " vec s " is the unit direction vector)"} newline size 24 {"So the total visibility is obtained by integrating over a sphere:"} newline newline {bold V}_pq = int csub {S} {bold J}_p(vec s){bold B}(vec s){bold J}^{%dagger}_q(vec s)d%OMEGA newline newline size 24 { "This is not very useful, so we project " bold B " onto " } newline size 24 { "the " %l%m " plane, tangential at the phase centre..." } newline

---
The Full-Sky ME
size 24 { "...and since " d%OMEGA = {d%l d%m} over sqrt{1-%l^2-%m^2} = {d%l d%m} over %n, } newline size 24 { "in the " %l%m " plane we get:" } newline newline {bold V}_pq = iint csub {%l%m} {bold J}_p(%l,%m){bold B(%l,%m)} over {%n(%l,%m)} {bold J}^{%dagger}_q(%l,%m)d%l d%m newline newline

---
Image-plane vs. uv-plane
size 24 { {bold J}_p " is composed of multiple effects: " {bold J}_p = {bold J}_pn {bold J}_{pn-1} ... {bold J}_p1} newline size 24 { ( {bold J}_pn " is \"at the antenna\", " {bold J}_p1 " is \"in the sky\"." )} newline size 24 { "Some " {bold J}"'s do not vary with " %l,%m " -- call them " ital "uv-plane effects." } newline alignr size 24 { "e.g. antenna gain, leakage." } newline size 24 { "Some " {bold J}"'s do vary with " %l,%m " -- call them " ital "image-plane effects." } newline alignr size 24 { "e.g. " bold K ", ionosphere, F.R." } newline size 24 {"Let's rewrite the " {bold J}_p " product as: " } newline size 24 { {bold J}_p = {{bold J}_pn ... {bold J}_{pk+1}} overbrace {"uv-plane only"} underbrace {{bold G}_p} {bold K}_p {{bold J}_{pk-1} ... {bold J}_p1} overbrace {"uv- & image-plane"} underbrace {{bold E}_p(%l,%m)} } newline size 24 { "Or in other words, " {bold J}_p(%l,%m) = {bold G}_p {bold K}_p(%l,%m) {bold E}_p(%l,%m) } newline size 24 { ("and depending on our particular M.E., " bold G " or " bold E " may be " equiv bold 1) }

---
Image-Plane vs.
uv-Plane Effects
{bold V}_pq = iint csub {%l%m} {bold J}_p(%l,%m){bold B(%l,%m)} over {%n(%l,%m)} {bold J}^{%dagger}_q(%l,%m)d%l d%m newline newline size 24 { "then becomes: "} newline newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold K}_p {bold E}_p bold B over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 { "(with everything under the " iint " being a function of " %l,%m ")" }

---
The Fourier Transform
size 24 { "and now expanding the " bold K " terms:"} newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({bold E}_p bold B over %n {bold E}^{%dagger}_q) e^{-{2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 { "for narrow fields " %n toward 1, " so:" } newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({{bold E}_p bold B {bold E}^{%dagger}_q} underbrace "\"apparent sky\"") {e^{-{2%pi%i}(u_pq%l+v_pq%m)}} underbrace "F.T. kernel" d%l d%m right ) {bold G}^{%dagger}_q
The integral is then exactly a 2D Fourier transform of the “apparent sky”.

---
The Fly In The Ointment
{bold V}_pq = {bold G}_p left ( iint csub {%l%m} ({bold E}_p {bold B}over %n {bold E}^{%dagger}_q)e^{{-2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m right ) {bold G}^{%dagger}_q
In the general case, the exponent is not quite an F.T. kernel.
Let's collect the pesky n-terms together, and define an “apparent projected sky”:
{bold B}_pq = %N_p {bold E}_p bold B {bold E}^{%dagger}_q N^{%dagger}_q = %N_pq {bold E}_p bold B {bold E}^{%dagger}_q newline size 24 { " where " %N_p = 1 over sqrt %n e^{-2%pi%i%w_p(%n-1)}, ~ %N_pq = %N_p {bar N}_q } newline size 24 { "(for narrow fields, " %N_p toward 1 " and may be neglected.)" }

---
Apparent Skies & Apparent Cohaerencies
size 24 {"We now have: "} newline {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold B}_pq e^{-{2%pi%i}(u_pq%l+v_pq%m)} d%l d%m right ) {bold G}^{%dagger}_q = {bold G}_p {bold X}_pq {bold G}^{%dagger}_q, newline size 24 { "where " {bold X}_pq = size 48 %fcall ( {bold B}_pq ) = size 48 %fcall ( %N_pq {bold E}_p bold B {bold E}^%dagger_q ) }
In other words, each antenna pair p-q measures an apparent cohaerency distribution Xpq(u,v) that corresponds to a 2D Fourier Transform of an apparent projected sky Bpq.
...at a single point in time!

---
Time Is Not On Our Side
Cohaerencies are sampled along a “uv track” over some period of time:
{bold V}_pq(t) = {bold G}_p(t) {bold X}_pq(t,u(t),v(t)) {bold G}^{%dagger}_q(t)
The true sky B is probably constant(?) in time
Image-plane effects (beam shapes, ionosphere) may vary in time.
For wide fields and non-coplanar arrays, the N term is non-negligible, and it depends on w which depends on time.
All this is especially relevant with new telescope designs.

---
The “Classic” Assumptions
size 24 {"The full-sky ME: " } {bold V}_pq = {bold G}_p {bold X}_pq {bold G}^{%dagger}_q, newline size 24 { "where " {bold X}_pq = size 36 %fcall({bold tilde B}_pq), ~{bold tilde B}_pq = %N_{pq} {bold E}_p bold B {bold E}^{%dagger}_q }newline newline size 24 { "If we assume that " {bold B}(t) equiv {bold B}, " and "{bold E}_p(t) equiv {bold E}_p equiv bold E, " and " %n toward 1, } newline size 24 "then all baselines will see the same, constant apparent sky: " newline {bold B}_{pq}(t) = bold E bold B {bold E}^%dagger equiv {bold tilde B} newline size 24 "and the array will sample one apparent cohaerency plane: " newline {bold X}_pq(t,u,v) equiv {bold X}(u,v)
Only under these assumptions is a single F.T. of the sky sufficient for the entire observation!

---
Conclusions
Under the “classic” assumptions, the visibilities measured by an array correspond to ONE cohaerency distribution X that is in an F.T. relationship with ONE apparent sky.
In the presence of non-trivial image plane effects, or with wide fields, each interferometer p-q measures its “own” cohaerency Xpq(t) corresponding to its “own” apparent sky Bpq(t) -- variable in time!
The K term becomes an F.T. kernel with narrow FOVs and coplanar arrays, but is “not quite” an F.T. otherwise.

---
Divide And Conquer
size 24 { {bold V}_pq = {bold G}_p left ( iint csub {%l%m} {bold K}_p {bold E}_p bold B over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q } newline newline alignc size 24 { "This is linear over " bold B", so if the sky is a sum of sources:" } newline {bold B}(%l,%m) = sum_s {bold B}_s(%l,%m), newline size 24 "then" newline newline {bold V}_pq = {bold G}_p left ( sum csub s iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_s over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m right ) {bold G}^{%dagger}_q newline newline size 24 {"And for some sources we can work out the integral exactly."}

---
A Sky Of Point Sources
size 24 {"For a point source " s " of flux " {bold B}_0s=1 over 2 left ( matrix{I_s+Q_s # U_s-%i V_s ## U_s+%i V_s # I_s-Q_s} right ) } newline size 24 { "the "bold B " distribution is a delta-function:"} newline size 24 { {bold B}_s(%l,%m) = { bold B}_0s%n%delta(%l-%l_s,%m-%m_s).} newline newline size 24 {"So for a sky of point sources:"} newline {bold V}_pq = {bold G}_p left ( sum csub s {bold K}_ps {bold E}_{ps} {bold B}_0s {bold E}^{%dagger}_{qs} {bold K}^{%dagger}_{qs} right ) {bold G}^{%dagger}_q, newline size 24 { "where " {bold K}_ps = {bold K}_p(%l_s,%m_s), " and "{bold E}_ps = {bold E}_p(%l_s,%m_s). }

---
Let's Build a Tree
"Assuming a perfect instrument again: " newline {bold V}_pq = sum csub s {bold K}_ps {bold B}_0s {bold K}^{%dagger}_{qs}
See Day3/demo1-predict-nps.py
We can already do one point source, adding more is just some for loops...
...and a Meq.Add node to sum the visibilities.
We'll put the sources on a grid.
Run the tree and make an MFS map.

---
Exercise 1: Complex Gains
"Let's add some gain terms: " newline {bold V}_pq = {bold G}_p left ( sum csub s {bold K}_ps {bold B}_0s {bold K}^{%dagger}_{qs} right ) {bold G}^%dagger_q
Use Day3/demo1-predict-nps.py as a starting point.
Add the gain terms from Day2/demo3-predict-ps-gain.py.
Make an MFS map.

---
Exercise 2: Adding Beams
alignc "Let's add a primary beam: " newline {bold V}_pq = {bold G}_p left ( sum csub s {bold E}_ps {bold K}_ps {bold B}_0s {bold K}^{%dagger}_{qs} {bold E}^%dagger_qs right ) {bold G}^%dagger_q newline "use " {bold E}(%l,%m) = cos^6 (1.5 cdot 10^-6 %nu sqrt {%l^2+%m^2})newline size 24 { "(i.e. same for all antennas)" } newline
Use the previous script as a starting point.
Make a per-channel map.

---
Code Reuse?
By now our scripts are getting rather complex.
On the other hand, we're reusing the same building blocks, e.g.:
  - point sources
  - Jones matrices
Good programming strives for maximum code reuse; good languages simplify this via modules, libraries, objects, etc.
TDL is Python, and Python is an excellent programming language.

---
Frameworks!
A tree is like assembly language – the nuts'n'bolts view of what's going on.
Pure TDL is like C – a higher level language, but still very close to what the “tree machine” is doing.
An OO framework provides abstraction, so you talk in terms of:
  - I have an interferometer array of N antennas
  - make me a point source here
  - make me the nodes to compute the source's uncorrupted visibilities at each baseline
  - apply this Jones matrix and give me the corrupted visibilities

---
Meow
(Measurement Equation Object Framework)
See Day3/demo2-nps-meow.py.
This is the equivalent of demo1.
Highlights:
  - we deal in “sky components”, “arrays”, “observations”
  - details of sources are hidden, it just gives us the visibility nodes
also provides convenient utilities for
  - GUI options
  - I/O records
  - imaging

---
Meow With Jones
Now let's add E and G terms
See Day3/demo3-nps-corrupt-meow.py.
We make CorruptComponents from components by adding a Jones corruption term.
Corrupt Components are also sky components, so they can be treated the same way.
Modularity:
  - sky models defined in one place...
  - Jones terms defined in another place...
  - main sim script just puts them together

---
...Meoooooooow
Extended sources?
See Day4/demo4-nps-ext-meow.py.
Small change: use GaussianSource in place of some PointSources.
Don't need to know the details of a Gaussian implementation, since we can just get the visibility nodes from the source.

---
“Well I'm liberal, but to a degree...”
-- Bob Dylan
Meow is just “a” framework, we do have others
We believe in creative pragmatic anarchy...
...so don't take any framework as gospel.
  - especially as it's a work in progress
  - your feedback will drive that progress!
Use them, or make your own, but be pragmatic:
  - if you feel if something is missing, think of how to improve it, and talk to the author
  - ideally, we want to fold your improvements back into the mainstream, for the benefit of others.

---
A “Real”-Life Example:
The CLAR

---
A Simple CLAR Sim
The CLAR primary beam is elevation-dependent
  - symmetric at zenith
  - broadened vertically as we track towards the horizon
Let's simulate a CLAR observation of 10 point sources, using the following m.e.:
See Day3/demo5-clar.py
ddd

---
A Simple CLAR Sim
The CLAR primary beam is elevation-dependent
  - symmetric at zenith
  - broadened vertically as we track towards the horizon
Let's simulate 10 point sources:
{bold V}_pq = sum csub s {bold K}_ps {bold E}_p(%l_s,%m_s) {bold B}_0s {bold E}^{%dagger}_q(%l_s,%m_s) {bold K}^{%dagger}_{qs} newline size 24 { {bold E}_p(%l,%m) = {bold E}_CLAR(%l,%m;El) ~~~~~ (El"=elevation") }

---
A Simple CLAR Sim
See Day3/demo5-clar.py
This defines a per-station, per-source E Jones term.
E Jones details are in clar_model.py.
We use pre-computed beam gains:
  - The vgain parameter is a Meq.Parm node
  - There's a ParmTable (*.mep) supplying vgain values (as a function of time)
  - These are precomputed by another script
    (clar_fit_dq.py)
  - ...but in principle could have come from anywhere.

---
A Simple CLAR Sim
Note also the “source model” option in the GUI.
This selects a function, which the script then calls to obtain a source model.
This a “compile-time” option
  - determines the kind of tree that is built
  - ...as opposed to run-time options, which determine what kind of request to give the tree.
Python makes this sort of thing easy, and it gives us a further degree of abstraction.

---
And Now For Something Completely Different:
Time & Bandwidth Smearing
size 24 { langle {bold J}_p (vec e {vec e}^{%dagger} ) {bold J}_q^%dagger rangle = {bold J}_p langle vec e {vec e}^{%dagger} rangle {bold J}_q^%dagger " ??"} newline alignl size 24 { "In effect, we've been computing " {bold V}_pq(t_0,%nu_0), " and assuming "} newline alignl size 24 { "that this close enough to the " ital "vector average" " over " %DELTA t,%DELTA%nu . } newline alignl size 24 { "This is OK as long as " {bold J}_p"s are sufficiently constant over " %DELTA t,%DELTA%nu .} newline alignl size 24 { "But as a minumum, " {bold J}_p " contains " {bold K}_p, "and :" } newline size 24 { {bold K}_p{bold K}^%dagger_q = exp({2%pi%i%nu} over c(u%l+v%m+w(%n-1)))} newline alignr size 20 { (uvw"'s change with " t, " longer baselines change faster") } newline alignl size 24 { "So even in the absense of any additional effects, " } newline size 24 { langle {bold K}_p bold B {bold K}^%dagger_q rangle_{%DELTA t,%DELTA%nu} ~ <> ~ {bold K}_p(t_0,%nu_0) bold B {bold K}^%dagger_q(t_0,%nu_0) } newline alignl size 24 { "This is usually known as time and bandwidth smearing." } newline alignl size 24 { "The effect goes up with " %DELTA t,%DELTA%nu,%l,%m, " and baseline length." }

---
Simulating Smearing
The same effect occurs with other Jones terms, such as ionospheric or tropospheric phase, etc. (hence, decohaerency time).
How to simulate?
The brute force approach:
alignl size 24 { "- Divide each " %DELTA t,%DELTA%nu " into " N times M " sub-intervals, and use" } newline size 24 {langle {bold V}_pq rangle_{%DELTA t,%DELTA%nu} approx 1 over NM sum csub {i,j} {bold V}_pq(t_i,%nu_j)}
See Day3/demo6-smear.py (and compare to demo2...)
  - Meq.ModRes changes resolution
  - Meq.Resampler averages back

---
So What's The Difference?
Run the tree and make an MFS map
  - 5x5=25 times more visibilities to compute, so it takes longer...
Hard to see anything in the map
(although you could subtract an older map, if you happened to have saved one...)
So let's build a differential tree instead, to compute
size 24 { {bold %DELTA}_pq = {bold V}_pq(t_0,%nu_0) - langle {bold V}_pq rangle_{%DELTA t,%DELTA%nu} }
...and write the deltas to the MS.

---
Interlude:
How To Make Your Tree Run Very Slow
There's a naïve way to compute the deltas:
  - subtract “predict” from “resamp”, and connect that to the sink.
Why is this so slow??
  - each “predict:p:q” tree is called twice, once at low res, once at high res.
  - ...so we're not using the node caches.
The right way to do it: parallel trees
See Day3/demo7-smear-diff.py.
Moral: reuse values, not nodes.

---
Differential Trees
(Or Simulations About Simulations)
Given infinite CPUs, we can implement M.E.'s of arbitrary precision.
In real life, we have to take shortcuts
(e.g. choosing time/freq intervals here).
The main question: how much error does a particular shortcut introduce?
  - given infinite mathematical skill, we could work it out analytically...
  - ...but given MeqTrees, we don't have to.

---
The Lowly Point Source
as a probe of the simulations universe
For single point sources, we can implement a very precise form of the ME.
For large-scale simulations, we're forced to implement an approximate ME (AME).
We can cheaply predict a grid of point sources:
  - with a precise ME
  - with an approximate ME
The difference tells you the error you make when using the AME.

---
Exercise 3:
A CLAR shortcut
Do we need per-station beams?
  - the beam depends on elevation
  - all antennas track the same point on the sky
  - ...so will have slightly different elevations
  - ...very slightly (array size is 30km)
Can't we just use an average beam?
"i.e. " {bold E} {bold B} {bold E}^{%dagger} " instead of " {bold E}_p bold B {bold E}^%dagger_q

---
Exercise 3:
A CLAR shortcut
Start with demo5-clar.py.
Insert the “grid model” from demo2.
Produce a tree to compute the delta-visibilities between:
  - the “precise” CLAR sim, with per-station beams Ep.
  - an approximate CLAR sim, using the same beam for all stations:
{bold E}_"avg" = 1 over N sum csub p {bold E}_p
Hint: you can reuse nodes freely.