ME3: Extended Sources,
Images, Image-Plane Effects
Objectives:
Learning to predict extended sources
Getting to grips with wide fields and n
Thinking about image-plane effects
Planting the seeds of some advanced topics and techniques
  - svn up ~/Workshop2006 please!!!

---
Prelude: Is There Such a Beast As “Corrected” uv-Data?
alignl size 24 { "Say we have a set of \"corrupted\" visibilities:" } newline {bold V}_pq={bold G}_p size 48 %fcall(%N_pq {bold E}_p{bold B}{bold E}^{%dagger}_q ){bold G}^{%dagger}_q newline alignl size 24 { "... and we know all of the " {bold G}_p, {bold E}_p, "and (of course) " %N_{p}"'s";} newline alignl size 24 { "then is there a way to obtain \"corrected\" visibilities " {bold V'} } newline size 24 { "such that " } {bold V'}_pq=size 48 %fcall({bold B})~~ ?? newline newline size 24 { " (or at the very least " {bold V'}_pq=size 36 %fcall(%N_pq {bold B} ) ") ???" } newline

---
NO!
uv-plane effects (the Gs) can be easily taken out:
alignl size 24 { "if " {bold V} = {bold G}_p size 36 %fcall({bold tilde B}) {bold G}^{%dagger}_q, " and we know " bold G,} newline alignl size 24 { "then we can derive " {bold V'} = {bold G}^{-1}_p {bold V} ({bold G}^{%dagger}_q)^-1 equiv size 36 %fcall({bold tilde B}) }.
image-plane effects are generally irreversible:
alignl size 24 { bold V =size 36 %fcall(%N_pq{bold E}_p{bold B}{bold E}^{%dagger}_q%N^%dagger_p) = size 36 %fcall({bold E}_p) circ size 36 %fcall(%N_pq{bold B}) circ size 36 %fcall({bold E}^{%dagger}_q)} newline alignl size 24 { "since convolution is, in general, irreversible." }

---
Correcting at a single point
alignl size 24 { "But we can correct for a single point " %l_0,%m_0: } newline bold V' = {bold E}_p(%l_0,%m_0)^{-1} bold V{bold E}^{%dagger}_q(%l_0,%m_0)^-1 "=" newline alignc "=" size 48 %fcall left (({bold E}_p(%l_0,%m_0))^{-1}{bold E}_p %N_pq bold B {bold E}_q^%dagger({bold E}^{%dagger}_q(%l_0,%m_0))^{-1} right ) newline alignc "=" size 48 %fcall(%N_pq bold B') newline newline alignl size 24 { "where " {bold B'}(%l_0,%m_0) = {bold B}(%l_0,%m_0)," but diverges further away." }
In general, uv data can only be “corrected” for a single point on the sky.
This is the motivation for facet imaging.
(There are some shortcuts...)

---
Divide And Conquer
size 24 { "Let's forget about the " bold G "s, as they're trivial to put in/remove." } newline size 24 { "(M.E.) " {bold V}_pq = iint csub {%l%m} {bold K}_p {bold E}_p bold B over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m = int csub{"sky"} {bold K}_p {bold E}_p bold B {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%OMEGA } newline newline alignc size 24 { "This is linear over " bold B", so if the sky is a sum of sources:" } newline size 24 { {bold B}(%l,%m) = sum_s {bold B}_s(%l,%m), " (or " {bold B}(vec %sigma) = sum_s {bold B}_s(vec%sigma) " )" }newline size 24 "then" newline {bold V}_pq = sum csub s {bold V}^{(s)}_pq = sum csub s iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_s over %n {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m newline size 24 {"And we can examine the integral for each source separately."}

---
Case 1. Point Sources
Point sources we have already done, their B is a delta function.
size 24 { {bold V}_pq = iint csub {%l%m} {bold K}_p {bold E}_p {bold B}_0 %delta(size 24{%l-%l_0,%m-%m_0}) {bold E}^{%dagger}_q {bold K}^{%dagger}_q d%l d%m ~ = "" } newline size 24 { alignc "" = ~ {bold K}_p(size 24{%l_0,%m_0}) {bold E}_p(size 24{%l_0,%m_0}) {bold B}_0 {bold E}^{%dagger}_q(size 24{%l_0,%m_0}) {bold K}^{%dagger}_q(size 24{%l_0,%m_0}) } ~= "" newline newline alignc "" = ~ {bold K}_p0 {bold E}_p0 {bold B}_0 {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
Product of five 2x2 matrices.
We can predict point sources perfectly.
Computationally practical for a limited number of sources.

---
Case 2. Extended Sources
And Patches
Any B that is not a delta-function gets interesting, especially if E is not trivial, and especially for wider fields (the “not quite an F.T.” problem.)
...but we need to solve this for two reasons.
Reason 1: spatially extended sources...
Reason 2: it is impractical to directly predict large numbers of fainter sources individually, so we need to organize them into “patches”, and find a faster way to predict a patch en masse.

---
First, Reduce To Center...
alignl size 24 {"Consider a source centered on direction " vec %sigma_0 ~~ (%l_0,%m_0), } newline alignl size 24 {"with the phase center at " vec %sigma=0. } newline size 24 { {bold V}_pq = int csub{"sky"} {bold K}_p(vec%sigma) {bold E}_p(vec%sigma) bold B(vec%sigma) {bold E}^{%dagger}_q(vec%sigma) {bold K}^{%dagger}_q(vec%sigma) d%OMEGA = ""} newline size 24 { "Let's integrate in the coordinate system " vec %sigma'=vec%sigma+vec%sigma_0, } newline size 24 { "and define " {bold tilde B}(vec%sigma) equiv {bold B}(vec%sigma+vec%sigma_0), ~{bold tilde E}_p(vec%sigma) equiv {bold B}(vec%sigma+vec%sigma_0): } newline size 24 { {bold V}_pq = int csub{"sky"} {bold K}_p(vec%sigma+vec%sigma_0) {bold E}_p(vec%sigma+vec%sigma_0) bold B(vec%sigma+vec%sigma_0) {bold E}^{%dagger}_q(vec%sigma+vec%sigma_0) {bold K}^{%dagger}_q(vec%sigma+vec%sigma_0) d%OMEGA' = ""} newline size 24 { "" = {bold K}_p(vec %sigma_0) left ( int csub{"sky"} {bold K}_p(vec%sigma) {bold tilde E}_p(vec%sigma) bold tilde B(vec%sigma) {bold tilde E}^{%dagger}_q(vec%sigma) {bold K}^{%dagger}_q(vec%sigma) d%OMEGA right ) {bold K}^%dagger_q(vec %sigma_0) = ""} newline size 24 { "" = {bold K}_p(%l_0,%m_0) left ( iint csub{%l%m} {bold K}_p {bold tilde E}_p bold tilde B over %n {bold tilde E}^%dagger_q {bold K}^%dagger_q d%l d%m right ) {bold K}^%dagger_q(%l_0,%m_0) } newline

---
...Where Life Gets Easier
{bold V}_pq = {bold K}_p0 left ( iint csub{%l%m} {bold K}_p {bold tilde E}_p bold tilde B over %n {bold tilde E}^%dagger_q {bold K}^%dagger_q d%l d%m right ) {bold K}^%dagger_q0
In other words, to predict a source at l0,m0, it is sufficient to predict it at the phase center (shifting E accordingly...), then apply the phase terms Kp0, Kq0 to “move” the source to its true position.
This is beautifully symmetric w.r.t. the ME for a point source:
{bold K}_p0 {bold E}_p0 {bold B}_0 {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0

---
So All We Need
To Figure Out Now...
...is how to predict extended sources at the phase center. We've simplified the problem considerably. If we now expand the K terms:
size 24 { {bold V}_pq = iint csub {%l%m} ({bold E}_p bold B over %n {bold E}^{%dagger}_q) e^{-{2%pi%i}(u_pq%l+v_pq%m+w_pq(%n-1))} d%l d%m } newline size 24 { "When " %n toward 1 ", this becomes a Fourier Transform:"} newline size 24 { {bold V}_pq = iint csub {%l%m} ({{bold E}_p bold B {bold E}^{%dagger}_q} underbrace "\"apparent sky\"") {e^{-{2%pi%i}(u_pq%l+v_pq%m)}} underbrace "F.T. kernel" d%l d%m }
...and we only require the “Weak Assumption” that n→1 over the extent of the source.

---
Or Even More Optimistically...
alignl size 24 { "If we also make the \"Strong Assumption\" that " } newline alignl size 24 { {bold E}_p approx {bold E}_p(0,0) " over the source, then " } newline {bold V}_pq = {bold K}_p0 {bold E}_p0 size 48 %fcall ( {bold B}_0 ) {bold E}^{%dagger}_q0 {bold K}^{%dagger}_q0
This is very good from a practical point of view, since:
F.T.'s are easier than strange integrals
phase shifts and (in the optimistic case) image-plane effects are applied in the same way to all kinds of sources
we only need to worry about predicting the source (or patch) at the phase center

---
The Bad News
This is only an approximation.
Error levels will depend on:
source flux (in a linear way, so we can talk about relative error);
patch/source size (because of the n term);
the variation in E over the extent of the patch.
We need to develop some feeling for how small the patches/sources need to be to make the error suitably small.
We can build some trees to simulate these errors (well this is actually good news, isn't it?)

---
Case 2:
“Analytic” Extended Sources
For some kinds of sources (e.g., a 2D Gaussian), we can write out the F.T. analytically.
size 24 { "i.e. given a set of source parameters that determine its " bold B } newline size 24 { "(for a Gaussian, this is its major/minor axis extent " %sigma_1,%sigma_2 ", " } newline size 24 { "position angle " %theta, " and integrated " I,Q,U,V " fluxes),"} newline size 24 { "we can immediately write out an expression for its " size 36 %fcall (bold B). } newline size 24 { "(The F.T. of a Gaussian is a Gaussian.)" }
Meow.GaussianSource implements the trees for this.
Only correct under the “Strong Assumption”, obviously.

---
Shapelets: The Ultimate
In Analytic Sources
The shapelet transform decomposes an image (in l,m) into a sum of shapelet basis functions:
Complex source structure can (potentially) be represented with relatively few low-order {cn} coefficients.
The basis functions sn have an analytic F.T.
Therefore, we can quickly compute the F.T. of a shapelet source, given a set of coefficients.
“Strong Assumption” required...
Just making its way into MeqTrees, so no demo...
alignl size 24 { b(%l,%m) = sum csub n c_n cdot s_n(%l,%m) }

---
Case 3: “Image” Sources
Finally, we can have an image – B (or perhaps just plain I) sampled on a RA/Dec (or other) grid.
An FFT gives us the F.T. on a regular uv grid:
size 24 { lbrace {bold B}_ij = {bold B}(%l_i,%m_j) rbrace ~~ %tendto csup "FFT" ~~ lbrace {bold X}_ij = size 48 %fcall(bold B)(u_i,v_j) rbrace }
This is done by the Meq.FFTBrick node.
The Meq.UVInterpol node then takes...
size 24 { ... u(t), v(t) " from one child, and interpolates" } newline size 24 { {bold X}(t,%nu)={bold X}left ( {%nu u(t)} over c,{%nu v(t)} over c right ) " within the " lbrace {bold X}_ij rbrace " \"brick\"" } newline size 24 { " (which it gets from the other child.)" }

---
Implementing An Image Source
Meow.FITSImageComponent implements the right combination of Meq.FFTBrick, Meq.UVInterpol, and Meq.FITSImage.
Images can also have a frequency axis, this is seamlessly propagated through the tree.
No demo – something is currently broken :(

---
Bonus Image:
The True nJy Sky

---
Image Sources &
Image-Plane Effects
"Given an image, " lbrace {bold B}_ij rbrace, " we can easily apply " bold E: newline {bold B}_pq = {bold E}_p bold B {bold E}^%dagger_q
This can be done in a simple tree:
  - the FFTBrick node expects a “brick” child.
  - this doesn't have to be an actual FITSImage node, but can also be any subtree, i.e. one that does some operations on the image.
If the Ep's are different per antenna, this is INSANELY expensive (an FFT per baseline!)

---
The Bhatnagar Approach:
Coming Soon To a Tree Near You?
size 48 %fcall ( {bold E}_p{bold B}{bold E}^%dagger_q ) = size 48 %fcall ( {bold E}_p) circ bold X circ size 48 %fcall ({bold E}^%dagger_q ) newline size 24 {"If " {bold E}_p " is sufficiently smooth, then " size 36 %fcall ({bold E}_p) " can be approximated " } newline size 24 {"with just a few low-order Fourier coefficients." }
Convolution with a “small” kernel can be computed directly, fairly cheaply.
...and in fact the interpolation function used inside UVInterpol to interpolate X to the uv track is a form of convolution.
So we can apply E's with a suitable modification to the convolution function.

---
n: Naughty, Nasty, Notorious, Nefarious, Nebulous, Noxious,
or Just Negligible?
The “Weak Assumption” is that n=1 over the extent of the source.
Let's make a differential tree to estimate the error that this assumption introduces.
General idea: make a test grid of point sources, then:
  - predict them perfectly in one branch.
  - predict them with (l,m,1) in the other branch.
The former are Meow.PointSources, how do we implement the latter?
...through OOP, of course!

---
A Naughty Direction
lmn's ultimately come from Meow.LMDirection.
We're going to derive a subclass from Meow.LMDirection
This subclass reimplements the n() function, which LMDirection uses to create its n node (which is subsequently used to make a K term).
The end result: a direction that “ignores” the normal n term, and uses 1 instead.
See Day4/NaughtyDirection.py.

---
Demo 1: So How Weak
Is The “Weak Assumption”?
Load up Day4/demo1-naughty.py.
This makes two sets of sources arranged in a “cross”:
  - Regular PointSources in one branch
  - PointSources with a NaughtyDirection in the other branch
You can select the grid stepping size – compare results for 1' and 60'.
Compare MFS and per-channel maps.

---
Mega-Exercise 3:
Replicating The Perley Movie
size 24 { "The ionosphere introduces two effects: Faraday rotation" } newline size 24 { bold F = "Rot" ("RM" over %nu^2), " and phase delay: " bold L = e^{-i%theta}. } newline alignl size 24 { "Both RM and " %theta " are proportional to TEC"(%l,%m).} newline alignl size 24 { "Let's simulate a TID (Travelling Ionospheric Disturbance)," } newline alignl size 24 { "by making " TEC(x,y) " constant + a moving 1D sine wave." } newline alignl size 24 { "(And each antenna looks up through a different " x,y " point.)"} newline alignl size 24 { "We'll make a grid of point sources, and apply " bold F " and " bold L.} newline alignl size 24 { "With a bit of luck, we can even force the imager to make " } newline alignl size 24 { "a series of time slices..."}