Day 2: Calibration & Polarization

---
What Is Calibration?
...according to Google
# The process whereby the magnitude of the output of a measuring instrument is related to the magnitude of the input force driving the instrument (ie Adjusting a weight scale to zero when there is nothing on it). (Course Material/Ultrasonics/CalibrationMeth/calibrationmethods.htm)
www.ndt-ed.org/GeneralResources/Glossary/letter/c.htm
# The process of adjusting an instrument or compiling a deviation chart so that its reading can be correlated to the actual value being measured.
www.omega.com/literature/transactions/volume1/glossary.html
# The process of choosing attribute values and computational parameters so that a model properly represents the real-world situation being analyzed. For example, in pathfinding and allocation, calibration generally refers to assigning or calculating appropriate values to be entered in impedance and demand items.
www.geog.leeds.ac.uk/staff/m.blake/magis/glossary/esriglos.htm
# (cal·i·bra·tion) (kal²[ibreve]-bra¢sh[schwa]n) 1. determination of the accuracy of an instrument, usually by measurement of its variation from a standard, to ascertain necessary correction factors. 2. measurement of the caliber of a tube.
www.mercksource.com/pp/us/cns/cns_hl_dorlands.jspzQzpgzEzzSzppdocszSzuszSzcommonzSzdorlandszSzdorlandzSzdmd_c_03zPzhtm
# Checking, adjusting and systematically standardizing the graduations of a device.
www.inkcartridgesworld.com/_glossary.html
# The process of establishing a set of values for correct operation.
www.blazepoint.co.uk/faq_label_printers_glossary.html
# A process that establishes, under specified conditions, the relationship between the values indicated by the measuring system, and the corresponding values of a quantity realised by a reference standard or working standard.
www.nzelectricity.co.nz/H9glossary.htm
# process of comparing an instrument's accuracy to known standards
www.tsgc.utexas.edu/stars/glossary1.html
# is defined as the process of quantitatively defining the system response to known, controlled signal inputs.
www.eumetsat.int/en/dps/helpdesk/glossary.html

---
...according to Noordam

---
...according to the
EoR KSG
EoR Signature???

---
Our Definition For Today...
Determining the properties of the sky and the instrument with sufficient accuracy.
“Taking out” (as much as possible) instrumental corruptions.
Subtracting known sources
...to find the noise (or at least to achieve our scientific objectives)

---
“Classic” Self-calibration
(for phases/gains)
alignl size 24 { "Assume this m.e.: " v_{pq} = g_p g^%star_q b e^{-2%pi%i (u_pq %l + v_pq %m + w_pq (%n-1))}} newline newline alignl size 24 {"1. Assume some source brightness, " b} newline alignl size 24 {"2. Derive \"model\" coherencies: " x_pq = be^{-%i%varphi_pq} } newline alignl size 24 {"3. Predict \"corrupted\" model: " x'_pq = g_p x_{pq}g^%star_q } newline alignl size 24 {"4. Find " g_p "s by fitting " x'_{pq} " to observed " v_{pq} } newline alignl size 24 {"5. Compute \"corrected\" visibilities: " v'_{pq} = v_{pq} {g_p^-1 (g_q^-1)^%star} } newline newline alignl size 24 {"The \"corrected\" visibilities should then correspond "} newline alignl size 24 {"to the \"true\", uncorrupted source."} newline

---
The M.E. Analogue
alignl size 24 { "Assume this m.e.: " {bold V}_{pq} = {bold G}_p {bold K}_p bold B {bold K}^%dagger_q {bold G}^%dagger_q } newline newline alignl size 24 {"1. Start with a model for the source, " {bold B}} newline alignl size 24 {"2. Derive \"model\" coherencies: " {bold X}_pq = {bold K}_p bold B {bold K}^%dagger_q } newline alignl size 24 {"3. Predict \"corrupted\" model: " {bold X}'_pq = {bold G}_p {bold X}_{pq}{bold G}^%dagger_q } newline alignl size 24 {"4. Find " {bold G}_p "s by fitting " {bold X}'_{pq} " to observed " {bold V}_{pq} } newline alignl size 24 {"5. Compute \"corrected\" visibilities: " {bold V}'_{pq} = {bold G}^{-1}_p {bold V}_{pq}({bold G}^{-1}_q)^%dagger } newline alignr size 24 { " (note that " ({bold G}^%dagger)^{-1} = ({bold G}^{-1})^%dagger ")" } newline newline alignl size 24 {"The \"corrected\" visibilities should then correspond "} newline alignl size 24 {"to the \"true\", uncorrupted source."} newline

---
Or In Broad Terms...
Predict corrupted visibilities
  - we already do this with Siamese
Fit to observed visibilities
  - solving for parameters of the sky and/or the instrument
(Optional: subtract bright sources)
Correct
Rinse & repeat
  - aka the “major loop”: source extraction, updating sky model, etc.

---
Correcting For Multiple Jones Terms
alignl size 24 { "Given an m.e. of the form:" } newline size 24 { {bold V}_pq = {bold J}_pn ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {bold J}^{%dagger}_qn } newline alignl size 24 { "the corrections need to be applied in reverse order:" } newline size 24 { {bold V}'_pq = {bold J}^{-1}_p1 ... {bold J}^{-1}_pn {bold V}_pq ({bold J}^{-1}_qn)^%dagger ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold J}^{-1}_p1 ... {{bold J}^{-1}_pn {bold J}_pn} underbrace {""=1} ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {{bold J}^{%dagger}_qn ({bold J}^{-1}_qn)^%dagger}underbrace{""=1} ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold X}_pq } newline newline alignl size 24 {"...and all matrix (non-)commutation rules apply." }

---
Limitations Of Correction
alignl size 24 { "Given an m.e. of the form:" } newline size 24 { {bold V}_pq = {bold J}_pn ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {bold J}^{%dagger}_qn } newline alignl size 24 { "the corrections need to be applied in reverse order:" } newline size 24 { {bold V}'_pq = {bold J}^{-1}_p1 ... {bold J}^{-1}_pn {bold V}_pq ({bold J}^{-1}_qn)^%dagger ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold J}^{-1}_p1 ... {{bold J}^{-1}_pn {bold J}_pn} underbrace {""=1} ... {bold J}_p1 {bold X}_pq {bold J}^{%dagger}_q1 ... {{bold J}^{%dagger}_qn ({bold J}^{-1}_qn)^%dagger}underbrace{""=1} ... ({bold J}^{-1}_{q1})^%dagger = "" } newline size 24 { "" = {bold X}_pq }
Matrix inversion has its pitfalls
What happens if J is singular?
  - and what physics does this correspond to?

---
Limitations Of Correction 2
If a Jones matrix is singular, then we don't have enough information to begin with
  - e.g. if a dipole gain is 0, then we haven't measured the EM field in one direction...
It is also possible for a Jones term to be ill-conditioned
  - numerical inversion of an ill-conditioned matrix breaks down due to precision limitations
  - e.g.: projection matrix of an aperture array (Tobia Carozzi)

---
Calibration Of An MS?
A model tree computes corrupted visibilities X'pq(t,)
  - we've used Siamese for this
MS DATA column contains observed data Vpq(t,)
We can take the difference and form up a 2 sum...
...and try to minimize it w.r.t. the solvable parameters.
Which is the same as fitting the model to the data, in a least-squares sense.
We can thus solve for any (reasonable) subset of parameters of a measurement equation.

---
A General Approach
To Fitting & Solving
A tree evaluating any m(t,) also depends on values of parameters up in the tree. We write this as:
m(t,;a,b,...)
Imagine a “magic” constant node a that returns not one, but two values: a and a+a.
Its parent, f, then returns f(a) and f(a+a)...
...and at the bottom we get m(t,;a) and m(t,;a+a)
size 24 { "From this we can estimate: " } newline size 24 { {%deriv m} over {%deriv a} approx {m(a+%delta a)-m(a)} over {%delta a}, ~~ {%deriv m} over {%deriv b} approx {m(b+%delta b)-m(b)} over {%delta b}} newline size 24 { "And then try to minimize or maximize " m... } newline size 24 { "(Which even a salmon can do.)" } newline

---
Calico
(Calibration Components)
I detect fringes...

---
Calico
Siamese's calibration cousin.
Same principle: build a measurement equation from a sky model + plug-in Jones modules.
  - Siamese modules are fully compatible
...but, modules can also specify their solvable parameters.
Calico provides a standard solving interface to these.
cd Workshop2008/Day2/Calico

---
Calico At Work: 3C286
3C286 is a standard WSRT calibrator
  - has significant QU (~10%)
We'll try to calibrate a short WSRT 1.4GHz observation.
  - ~15 mins at 10 sec. integration
Pristine copy:
cp -a (/net/birch)/data/oms/Workshop2007/3C343.MS .
(/apps/Timba/data on jop0x)

---
Viewing MSs
Load calico-view-ms.py
Select MS: 3C286-10705290.MS
  - antenna subset: 1:14
  - do not invert phases
Compile, load bookmarks for “inspect input visibilities”, and also for a few individual baselines.
Select “view MS”, inspect results...
Make an image
  - uniform weight, IQUV, average all channels

---
Thinking About Polarization 1
Diagonal Jones matrices will intermix I↔Q and U↔V:
Off-diagonal terms will intermix IQUV
Pure real terms won't touch V
  - e.g. a rotation matrix mixes QU, but not V
size 22 { left ( matrix{a_x # 0 ## 0 # a_y} right ) left ( matrix{I+Q # U+%i V ## U-%i V # I-Q} right ) left ( matrix{b_x # 0 ## 0 # b_y} right ) = left ( matrix{(I+Q)a_x b_x # (U+%i V)a_y b_y ## (U-%i V)a_x b_x # (I-Q) a_y b_y } right ) } newline alignl size 24 { " - e.g. " a_x <> a_y " causes instrumental polarization: " I rightarrow Q } newline alignl size 24 { " - e.g. phase difference transfers " U rightarrow V }

---
Thinking About Polarization 2
WSRT is an equatorial mount, so (to first order) it only has diagonal Jones terms
  - if the source is unpolarized, we can ignore the off-diagonal correlations
  - for off-center sources, we do have significant instrumental Q (on the diagonal)
  - (and in fact, there are small off-diagonal terms: “polarization leakage”)
With an alt-az mount, the sky rotates, so you'll see instrumental Q and U.
Thinking in terms of matrices will help you understand everything about polarization!

---
What Causes
Polarization Leakage?
Simple errors in dipole geometry:
    - these vary in time (slowly) due to the telescope mechanically deforming as it elevates
Electromagnetic cross-talk:
Both cases correspond to small values off the main diagonal of J
size 24 { %psi rightarrow }
size 24 { bold J = left ( matrix{cos %phi # - sin %phi ## sin %psi # cos %psi} right ) }
size 24 { leftarrow %phi }
size 20 { bold J = left ( matrix{g_xx # g_xy ## g_yx # g_yy} right ) ~~ binom{g_xx,g_yy rightarrow 1}{g_xy,g_yx rightarrow 0 }}

---
Calibrating 3C286
Load calico-286.py and look at Options
This is the M.E. we're going to use:
  - G (diagonal): short-term phase and gain variations
  - B (full 4-element): bandpass and pol. leakage
Unlike simulations, neither G or B is all that physical – each combines several physical effects
  - we don't care, as long as there's enough terms in our model to account for the physics
{bold V}_{pq} = {bold B}_p {bold G}_p {bold X}_pq {bold G}^%dagger_q {bold B}^%dagger_q

---
The Local Sky Model
Instead of pretty grid, we obviously want to calibrate on a realistic sky
The LSM module will read in a file and create a sky model based on it.
  - various formats supported
lsm286.txt is our model for this calibrator
  - cat lsm286.txt

---
Lost In TDL Options?
All options you set in the Options and TDL Exec windows are stored to a file called .tdl.conf (in the current directory)
A sensible copy of this file is in tdl.conf.orig
So if you completely mess up your Options, exit the browser and do
  - cp tdl.conf.orig .tdl.conf
  - ...to revert to the original settings.

---
MS/data selection options
This menu (in TDL Exec) determines what subset of the data we solve for
  - Input column is always DATA (for observed data)
  - Select channels 8 through 56, step 1
  - No Hanning tapering
  - “Data description ID” determines the spectral window. Pick one...

---
Step 1: Solving For G
G represents receiver gain/phase
  - diagonal (i.e. no cross-terms)
  - same across all channels
  - would like a separate solution per timeslot.
Build the tree, and open up the “Calibrate G diagonal terms” option.

---
Tiles And Solution Intervals
We go through the MS in chunks of time called tiles (a full MS wouldn't fit in memory...)
  - a tile contains N consecutive timeslots, and all [selected] channels of a spectral window
By default, each parameter has one solution per tile (constant or polynomial in time/freq)
  - but you can use a smaller solution interval via the “solution subinterval” option. This cannot be be bigger than the tile itself.
Bigger tiles are (to a point) faster, but too big can lead to poor convergence.

---
Step 1: Solving For G
Set “solution subinterval (time)” to 1
Set tile size to e.g. 20
Load the “inspector:G” and “inspect corrected data” bookmarks
Run “Calibrate G diagonal terms”
Watch the χ2 display at the bottom of the browser window.

---
MEP tables
Parameter solutions are stored in MEP (ME Parameter) tables.
  - these are called “*.mep” or “*.fmep”, and are generally kept within the MS directory
Once a solution is stored in the table, it is reused in all subsequent runs
  - so we can go on and solve for B, while including our G estimate in the predict
To clear out solutions and start anew:
  - rm -fr xxxxx.MS/*mep

---
Step 2: Solving For B (diagonal terms)
Open up “Calibrate for B diagonal terms”
We want separate solutions per each channel, for all timeslots.
  - set “solution subinterval (freq)” to 1
  - set tile size to 100
Load the “inspect corrected data” bookmarks, and some “B diagonal terms”
Run “Calibrate B diagonal terms”
Observe results... check also the XY/YX residuals

---
Step 3: Solving For B (off-diagonal terms)
Open up “Calibrate for B off-diagonal terms”
Select a simultaneous solution for B diag.
Run “Calibrate B off-diagonal terms”
Observe results... check also the XY/YX residuals

---
A More Serious Case: 3C343
Field is dominated by two bright sources:
  - 3C343.1 (~6 Jy) at phase center
  - 3C343 (~1.8 Jy) off-center
  - see lsm343.txt
Significant instrumental Q
  - we will ignore the cross-correlations
12-hour WSRT observation, 03/08/2000
64 channels ~ 1.2 Ghz (we use 26)
Pristine copy:
cp -a (/net/birch)/data/oms/Workshop2007/3C343.MS .
(/apps/Timba/data on jop0x)

---
Step 0: Standard Selfcal
Let's try solving for just a central source
  - lsm343.txt contains our Local Sky Model
  - cp lsm343.txt lsm343-1.txt
  - edit lsm343-1.txt: remove the second source
Go into Options|Sky model, and select lsm343-1.txt
Load “inspector:G” and “inspect residuals”
Try a solution for “G diagonal terms”, make a residual image
The M.E. here is:
{bold V}_{pq} = {bold G}_p {bold K}_p bold B {bold K}^%dagger_q {bold G}^%dagger_q = {bold G}_p {bold X}_pq {bold G}^%dagger_q

---
Step 1: A Two-Source Model
Go into Options|Sky model, and select lsm343.txt again
Load “inspector:G” and “inspect residuals”
Run a solution for “G diagonal terms”, make an image.
The M.E. here is:
{bold V}_{pq} = {bold G}_p ({bold X}^(1)_pq + {bold X}^(2)_pq) {bold G}^%dagger_q

---
Step 2: Bandpasses
{bold V}_{pq} = {bold B}_p {bold G}_p ({bold X}^(1)_pq + {bold X}^(2)_pq ) {bold G}^%dagger_q {bold B}^%dagger_q
We split out separate Jones terms according to their time/frequency behaviour:
  - G represents a fast-varying gain/phase term w/o a frequency dependence
  - B represents a slow-varying bandpass term, with a frequency dependence
Load some bookmarks for “B diagonal terms”, load “inspect residuals”
Run a solution for B diagonal terms, make an image

---
The Difficulty With 3C343
The off-center source (3C343) contaminates selfcal solutions, must be included in sky model
3C343 is not subtracted cleanly because...
...it has a different phase/gain
  - actually, all sources in the field do, but 3C343 is bright enough to make this a real problem
This is very awkward for “classic” calibration, at least without peeling

---
Step 3: Differential Gains
{bold V}_{pq} = {bold B}_p {bold G}_p ({bold X}^(1)_pq + {bold E}^(2)_p {bold X}^(2)_pq {bold E}^{(2)%dagger}_q) {bold G}^%dagger_q {bold B}^%dagger_q
This assigns a separate beam gain E to 3C343
  - will also account for phase difference, and for instrumental polarization
Load “inspect:E”, load “inspect residuals”
Run a solution for E diagonal terms, make an IQUV image
  - also look at E phases
  - note instrumental polarization

---
Exercise: Wrong Sky Model
We'll start with the wrong sky model
cp lsm343.txt lsm343-1.txt, edit lsm343-1.txt, and change Q of 3C343.1 to 0.6 (i.e. ~10% polarized)
Clear out previous calibrations:
  - rm -fr 3C343.MS/*mep
Repeat solutions for G-diag, B-diag, E-diag
  - pay attention to residuals
  - make images as you go
Think about what we should see at the end. Can we even expect to calibrate?

---
Limitations Of Selfcal
a.k.a. self-alignment (Hamaker)
alignl size 24 { "Classic selfcal can't fix the brightness scale:" } newline size 24 { v_{pq} = g_p g^%star_q b e^{-%i%phi} = (g_p y^-1)(g_q y^-1)^%star b y^2 e^{-%i%phi} " for any real " y.} newline newline alignl size 24 {"The M.E. analogue is:" } newline size 24 { {bold V}_{pq} = {bold J}_p {bold X}_pq {bold J}^%dagger_q = ({bold J}_p {bold Y}^-1) ({bold Y} {bold X}_pq {bold Y}^%dagger) ({bold J}_q {bold Y}^-1)^%dagger } newline alignr size 24 {"for any non-singular matrix " {bold Y}. }
So, we can only “know” the sky to within a (non-singular) Jones factor of Y.
What can this do to polarization?
  - anything...

---
Thinking About Polarization 3
Diagonal Jones matrices will intermix I↔Q and U↔V
Off-diagonal terms will intermix IQUV
So, starting with an unpolarized source, I flux can be moved into Q, Q can be rotated into U, and U can be phase-shifted into V.
size 24 { left ( matrix{I # 0 ## 0 # I} right ) rightarrow left ( matrix{I+Q # 0 ## 0 # I-Q} right ) rightarrow left ( matrix{I+Q # U ## U # I-Q} right ) rightarrow left ( matrix{I+Q # U+%i V ## U-%i V # I-Q} right ) }

---
The Evil Leprechaun
Principle
If evil leprechauns were to come and change your telescope in the middle of the night, would you notice?
  - without knowledge of the sky, that is.
...not if they changed them all by the same factor of Y.
  - e.g.: rotate all dipoles by the same angle
  - e.g.: change gain of all X dipoles
  - etc.
Moral: we can only get so far without known calibrators.